## Slide 1: 数字逻辑设计及应用
数制与编码（CH2）
数字电路（CH3）
组合逻辑设计原理（CH4）
组合逻辑设计实践（CH6）
时序逻辑设计原理（CH7）
时序逻辑设计实践（CH8）
存储器—ROM,RAM（CH9）
A/D、D/A转换器（补充）
期末涉及较少
半期考试之后的授课内容都在考试范围

## Slide 2
CH2、CH3、CH9、A/D、D/A转换器
组合逻辑
  CH4：4.1~4.3、4.4（static hazard）
  CH6: 6.4~6.10
时序逻辑
  CH7：7.1~7.5
  CH8：8.2、8.4、8.5
题型：
  填空、选择
  设计、分析：含门级、器件级，器件级的设计会给出功能表及引脚图，综合只要求会用D触发器完成。

## Slide 3: CH9 ROM、RAM
容量的表达：2n×b bit
  n位地址可确定2n个数据单元，每个单元有b位。
ROM用于组合逻辑函数的实现
  待实现函数的输入变量接ROM的地址端
  b位输出就可实现b个组合逻辑函数。
存储器的扩展，构成具有更大容量的存储器
  字、位扩展

## Slide 4: A/D、D/A转换
D/A转换：
若比例系数为1，则
若比例系数为正，则
输入数字值只有LSB为1时，输出电压是
1个Δ

## Slide 5
A/D转换：量化、编码
  量化阶梯的等级单位Δ与编码位数n的关系，量化的归化值mΔ对应的输出数字值是m的n位二进制值。
对于ADC，给定输入模拟量、Δ等值能计算输出的数字量；
对于DAC，给定Δ、输入数字量，能计算输出的模拟电压。反之亦然。

## Slide 6: 组合逻辑电路
CH4：基本概念在组合逻辑电路的分析及综合中的运用
  真值表、标准式、列表表达式（涵盖最小项、最大项性质）等表达逻辑功能的形式
  化简：公式法、卡诺图
  组合逻辑电路的基本形式：与或（与非-与非）、或与（或非-或非）、甚至“与或非”结构
  判断电路是否有冒险以及如何消除
  时序图的分析、绘制
  利用已有知识分析、综合组合逻辑电路
时序逻辑状态机的次态电路和输出电路是由组合逻辑构成，所以这部分内容是隐含在时序分析和设计中的。

## Slide 7: 组合逻辑电路
CH6：MSI的基本功能及应用
  译码器、MUX：基本功能以及在组合逻辑电路实现的应用
  编码器、三态器件
  异或门：表达式、特点，实现奇偶校验（parity circuit）及生成奇偶校验码（odd parity , even parity）、等值比较
  比较器和数值比较器：功能
  加法器：全加器
  组合逻辑分析、设计：与时序电路结合方式（次态逻辑、输出逻辑）

## Slide 8: 组合逻辑电路的综合
根据设计要求选择合适的实现方式
  门级，要求最简模式（“最小和”或者“最小积”）
  器件级，根据功能选择
    比如，运算类、码转换类、奇偶校验电路、具有比较性质等的，需要考虑加法器、比较器、异或门等有专用性质的部件
    译码器、MUX、ROM则可以用作通用性质的组合逻辑实现
  某些信号带有选择或控制特点的，要考虑正确的门电路
    与（与非）门——一般对应“全有效才有结果”情况
    或（或非）门——一般对应“有一个有效就有结果”情况
    异或（异或非）门——信号有“原变量”和“反变量”需要

## Slide 9: 时序逻辑电路
1、时序逻辑电路的表达及相关概念
状态—当前状态（现态）、次态（下一状态）
状态变量
同步时序电路的模块分割—次态逻辑、存储器、输出逻辑，Moore型、Mealy型时序电路的特点
2、时序逻辑电路的基本器件
锁存器、触发器功能及特征方程
分类：S-R、D、J-K、T
功能：存储1位二进制数，电路中代表一位状态变量
掌握基本器件的逻辑符号、触发方式（脉冲触发、边沿触发）等基本概念。
3、时序逻辑电路MSI（74*163、74*169、74*194…）

## Slide 10: 3、时序逻辑电路的分析
含触发器和组合电路构成的器件级电路、MSI加上组合电路的组件级电路。
能正确划分出电路的三大部分，分别写出电路的激励方程（excitation equation）、转换方程(transition equation)、输出方程。
根据转换方程、输出方程写出转换/输出表(transition/output table)，并给状态取名(state assignment)写出状态/输出表。
能画出状态图，符合状态转换的互斥性及完备性。
能根据转换方程、输出方程或表画出时序图。

## Slide 11
对于计数器等构成的时序电路，正常的状态转移是单循环的，有部分未用状态可能会回到主循环，有的不会。输入一般是控制类，清零、装数、初始值输入……，输出是计数输出，进位输出。
  触发器构建的计数器、163等MSI计数器
  序列的产生
  自校正的检测及修正
移位寄存器构成的电路，注意数据移动的方向与数据位的高低命名有关，每位寄存器之间都是首尾相连，中间不会插入其他部件。
  环形计数器、扭环计数器（约翰逊计数器）、序列产生

## Slide 12: 4、同步时序电路的设计
序列检测、位序列发生、计数器或以某种顺序发生变化等。
重要的第一步：按照设计要求，找出电路中可能的状态，每个状态表明发生的事情朝着解决问题的方向进行。
若采用触发器和组合电路等基本器件建立电路，写出状态/输出表或转移列表，确定触发器后进行状态赋值，得转移/输出表、利用选用的触发器的应用表构建激励表，建立激励方程、输出方程。注意“未用态”的处理
若采用MSI组件，正确设置相关的级联输入/输出、控制端、建立所需的反馈电路等。

## Slide 13
序列检测：
（1）基本触发器加门电路构成，从状态表或状态图着手。按照序列被检测出0位、1位、2位…的顺序定义电路的状态。
（2）移位寄存器法
位序列发生：
  计数器法—基本触发器加门电路构成
  计数器-译码器法
  计数器-数据选择器法
  计数器-ROM
  移位寄存器法

## Slide 14
计数器：按照给定的模值用触发器或者MSI构建同步时序计数器
  升序、降序（触发器模式或者特定的MSI）
  MSI计数器的应用及级联应用
寄存器及移位寄存器
  功能、移位的概念
  环形计数器（n位的模为n，需要n个触发器）
  Johnson计数器（ n位的模为2n，需要n个触发器）
其它同步时序电路

## Slide 15: examples
3. If an J-K flip-flop with J=1 and K=1 has a 10kHz clock input, the Q output is a ( 5k ) Hz square wave.
5. If we observed the waveforms of output Q1、Q2、Q3 of three flip-flops of a counter as the Figure 1, the modulo of the counter should be ( 6 ).
CP
Q1
Q2
Q3

## Slide 16
6. State/output table for a sequential circuit is shown as table 1. X is input and Zn is output. Assume that the initial state is S0, if the input sequence is X=01011101, the output sequence should be ( 11000100 ).
Table 1 State/output table |  | 
 | X | 
Sn | 0 | 1
S0 S1 S2 S3 | S0/1 S1/0 S2/0 S2/0 | S1/1 S2/0 S0/0 S0/0
Sn+1/Zn |  | 

## Slide 17
8. A 4-bit linear feedback shift-register (LFSR) counter with no self-correction can have ( 15 ) normal states.
10. When the input is 01000000 of an 8 bit DAC, the corresponding output voltage is 2V. The output voltage range for the DAC is ( 0 ~ 7.97 )V.

## Slide 18
1. If a 74x85 magnitude comparator has ALTBOUT=AGTBOUT=0, AEQBOUT=1 on its outputs, the cascading inputs are ( B ).
A) ALTBIN=0, AEQBIN=0, AGTBIN=0
B) ALTBIN=0, AEQBIN=1, AGTBIN=0
C) ALTBIN=1, AEQBIN=0, AGTBIN=1
D) ALTBIN=1, AEQBIN=1, AGTBIN=1

## Slide 19
3. An asynchronous counter differs from a synchronous in ( B ).
A) the number of states in its sequence
B) the method of clocking
C) the type of flip-flop used
D) the value of the modulus

## Slide 20
5. The capacity of a memory that has 10 bits address bus and can store 8 bits at each address is ( B )bits.
A) 1024 B) 8192 C) 80 D) 256

## Slide 21
A D Latch and a D Flip-flop are shown in Figure 3. The waveforms of a clock CP and an input D are shown in Figure 4. Assume the initial state of Q is 1. Try to draw the waveforms of Q of the D Latch and the D Flip-flop. Ignore the delay of the circuit.

## Slide 22
Design a variable modulus counter only with 74x163, which will be a module-6 counter when the input control signal M = 1 or a module-8 counter when M = 0. The states of module-6 counter should be（11,12,13,14,15,0）.The states of module-8 counter should be (9,10,11,12,13,14,15,0）. (10’)
(1)Please write out the input equations of LD_L, A, B, C, D. ( 5’)
(2)Draw the circuit line linked of 74x163.(5’)

## Slide 23
the input equations:
LD_L=Q3
D=A=1
C=0
B=M
M=1
1011
1100
1101
1110
1111
0000
M=0
1001
1010
1011
1100
1101
1110
1111
0000
Q3 Q2 Q1 Q0
Q3 Q2 Q1 Q0
74×163
QA
14
QB
13
QC
12
QD
11
RCO
15
A
3
B
4
C
5
D
6
ENP
7
ENT
10
LOAD
9
CLR
1
CLK
2
VCC
GND
M
Q0
Q1
Q2
Q3

## Slide 24: 15-16-2 exam
Assigning 0 to Low and 1 to High is called positive logic. A CMOS 2-input XOR gate in positive logic is called （ XNOR或 同或 ）gate in negative logic.
When the input of an 8 bit DAC is 01000000, the corresponding output voltage is 1.28V. The range of output voltage for the DAC is 0V~ ( 5.1 )V.
To design a "01101100" serial sequence generator by shift registers, we need a ( 5 )-bit shift register as least.

## Slide 25
For the following latches or flip-flops, can NOT be used to form shift register. （ B ）
  A) edge-triggered J-K flip-flop
  B) D latch with enable
  C) master/slave S-R flip-flop
  D) T flip-flop

## Slide 26
Which state in Figure 2.4 is NOT ambiguous. ( D )
  A) state A B) state B C) state C D) state C and state D

## Slide 27: 组合电路设计题
Design a combinational circuit with two 2-bit unsigned numbers inputs, A (A=A1A0) and B (B=B1B0), and a 4-bit unsigned number output Y (Y=Y3Y2Y1Y0), and to realize the function Y=2A+3B.
Question:
  Please write the truth table for the circuit.

## Slide 28
A1 | A0 | B1 | B0 | Y3 | Y2 | Y1 | Y0 | A1 | A0 | B1 | B0 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 29
Find the minimal sum-of-products （最简积之和）expression of Y3.
  Solution: Y3=B1B0+A0B1+A1B1+A1A0B0
The circuit can be built with a single 74x283 and no other gates. Draw the logic diagram for the circuit.
  C0 + (A0 + B0) + 2(A1 + B1) + 4(A2 + B2) + 8(A3 + B3) = S0 + 2S1 + 4S2+ 8S3+ 16C4
  Where (+) = plus.

## Slide 31: 时序电路设计II题
Construct a minimal state/output table for a Mealy sequential machine, that will detect the following input sequences: X=1010 or 1000. If input sequence X=1010 is met, cause Z1=1. If input sequence X=1000 is met, cause Z2=1. Each input sequence may overlap with itself or the other sequence. Please describe the state meaning and finish the minimal state/output table.

## Slide 32
State meaning | S | X | 
 |  | 0 | 1
Initial | A | A，00 | B,00
收到1 | B | C，00 | B，00
收到10 | C | D，00 | E，00
收到100 | D | A．01 | B，00
收到101 | E | C，10 | B，00
 |  | S*, Z1 Z2 | 

## Slide 33: 16-17-1 term
填空
4. Parity circuit can be used to detect errors during data transfer. Suppose that a 9-bit parity code with 8-bit information data and 1-bit parity is implemented in one data transfer system and the receiver get a data string 010011001 without error indicated, then the parity circuit realize a ( even ) (odd/even) parity.
8.A sequential circuit whose output depends only on its state is called a ( moore) state machine.

## Slide 34: 选择
4. Which of the following statements is CORRECT? ( D )
A. An edge-triggered D flip-flop never goes into metastable status.
B. A master/slave J-K flip-flop keep the current status when input J=1 and K=1.
C. if S is asserted, an S-R latch is forced to logic stats Q=1.
D. A D latch will follow the input as long as the control input C is active.

## Slide 35: 设计
V. Design an “101110” sequence generator with the shortest path self-correction only using one 74x194 and one 74x151. 74x194 will work in shift left mode. QA of 74x194 will be the sequence output. (18’)
(1) Fill out LIN in the simple transition table for 74x194. [7’]
(2) Write out the maxterm list of the feedback function for LIN. [1’]
(3) Fill out the K-maps. [3’]
(4) Draw the logic circuit diagram. [7’]

## Slide 36: 自校正的移位状态转移图
1011
0101
1010
1101
0111
1110
0000
0001
0010
或
0011
0100
1001
左移：LIN→QD→QC→QB→QA→反馈电路→LIN
QA QB QC QD
0110
1000
1100
1111