## Slide 1: Chapter 4 Combinational Logic Design Principles
本章重点
1、开关代数：公理、定理、逻辑电路的函数表达
2、组合电路的分析：组合电路的结构、逻辑表达式、真值表、时序图等。
3、组合电路的综合（设计）：逻辑抽象定义电路的功能，写出逻辑表达式，得到实际的电路。

## Slide 2: Chapter 4 exercises
The first homework
4.4 4.5 4.6 4.7(a,h) 4.9(b, d, f)
4.25 4.28 4.35
The second homework
4.15(a, c, e) 4.18(c, d) 4.47 4.54
4.55 4.56 4.59(d, e)

## Slide 3: Combinational logic circuit
The outputs depend only on its current inputs.
Any combinational function can be specified as a truth table or a Boolean expression.
In 1854, George Boole, two-valued algebraic system -- Boolean algebra
In 1938, Claude E. Shannon(1916-2001) adapt Boolean algebra to analyze and describe the behavior of circuits built from relays –switching algebra.
Shannon

## Slide 4: 4.1 Switching Algebra
Boolean values : 0, 1
Boolean operators ：+, ·, ’
1、Axioms
Symbolic
AND operation
(logic amplification)
OR operation
(logic addition)

## Slide 5: 2. Single Variable Theorems
Proofs by perfect induction
all values of the variable are substituted in the equation of a theorem , if it is true for both side of the equal sign, then the theorem is proved.
Identities(自等律)
Null elements (0-1律)
Idempotency (同一律)
Involution (还原律)
Complements (互补律)
(T1) X+0=X (T1’) X·1=X
(T2) X+1=1 (T2’) X·0=0
(T3) X+X=X (T3’) X·X=X
(T4) (X’)’=X
(T5) X+X’=1 (T5’) X·X’=0

## Slide 6: 3. two-and three-variable theorems
(T6) X+Y=Y+X (T6’) X·Y=Y·X
(T7) (X+Y)+Z=X+(Y+Z) (T7’) (X·Y)·Z=X·(Y·Z)
(T8) X·Y+X·Z=X·(Y+Z) (T8’) (X+Y)·(X+Z)=X+Y·Z
commutativity（交换律）
Associativity
（结合律）
Parenthesization or order of the terms in a logical sum or logical product is irrelevant.
Distributivity
（分配律）
Operating priority: prime(’), parentheses, AND, OR
logical multiplication distributes over logical addition
logical addition distributes over logical multiplication

## Slide 7
(T9) X+X·Y=X (T9’) X·(X+Y)=X
(T10) X·Y+X·Y’=X (T10’) (X+Y)·(X+Y’)=X
(T11) X·Y+X’·Z+Y·Z=X·Y+X’·Z
(T11’) (X+Y)·(X’+Z)·(Y+Z)=(X+Y)·(X’+Z)
covering（吸收律）
Combining
（组合律）
consensus（一致律）
T9、T9’、T10、T10’: be used to simplify logic functions.
Y·Z and (Y+Z) term are the redundant terms in the expression.
Supplement：
A+A’B=A+B （消因律）
A’+AB=A’+B

## Slide 8: 4. n-variable theorems
T13--- equivalent transform between “AND-NOT” and “NOT-OR”.
T13’--- equivalent transform between “OR-NOT” and “NOT-AND”.
Exp. ：G=X’·Y+V·W’·Z ——— =？
(T12) X+X+…+X=X (T12’) X·X·…·X=X
(T13) (X1·X2·……·Xn)’=X1’+X2’+……+Xn’
(T13’) (X1+X2+……+Xn)’=X1’·X2’·……·Xn’
DeMorgan theorems
Generalized idempotency
(广义同一律)
DeMorgan theorems

## Slide 9
T14—Generalized DeMorgan’s theorem (也称为“反演定理”), get the complement of a logic expression (inverse function)。
  keep the original operating order;
  complement all variables;
  swapping ‘0’ and ‘1’;
  swapping ‘+’ and ‘·’
  （the expression in brackets with a prime must keep the prime in the inverse function.）
exp：give the inverse function of the equation :
F=[(A·B’+C)·E]’+G’
(T14) [F(X1,X2,……,Xn, + , · )]’=F(X1’,X2’,……Xn’, · , +)

## Slide 10
finite induction
（1）proving the theorem is true for n=2;
（2）then proving that if the theorem is true for n=i, then it is also true for n=i+1.
(T15) F(X1,X2,…,Xn)=X1·F(1,X2,…,Xn)+X1’ ·F(0,X2,…,Xn)
(T15’) F(X1,X2,…,Xn)=[X1+F(0,X2,…,Xn)] ·[X1’+F(1,X2,…,Xn)]
(Shannon’s expansion theorems)

## Slide 11: 5. Duality
Any theorem or identity in switching algebra remains true if 0 and 1 are swapped and ‘·’ and ‘+’ are swapped throughout.
a logic expression： F(X1,X2,……,Xn, ’ , + , ·)
its duality：FD=F(X1,X2,……,Xn, ’ , · , +)
X·Y———X+Y 0———1
Exp.：find the duality expression .
F=(A·B+A’·C)’+1·B
duality
duality
unchanged
swapped

## Slide 12: Properties of duality
inverse function and duality：
[F(X1,X2,……,Xn, + , · ,’)]’= FD(X1’,X2’,……,Xn’, · , + ,’)
logic convention & duality :
  For a logic function, its positive logic expression and negative logic expression are duality.
  That means:
    positive logic negative logic
    AND = OR
    OR = AND
    NAND = NOR
    NOR = NAND

## Slide 13: 6. Using switching algebra in minimizing logic function
Exp.：
（1）F=AD+AD’+AB+A’C+BD+AB’EF+B’EF
（2）F=A·（B’+C）’·（BC）’
（3）F=AB+AC’+B’C+C’B+CD’+BD’
+ADE(F+G)

## Slide 14: 7. Standard representation of logic functions
truth table
Algebraic representation
canonical sum
canonical product
……
How to describe the relation between input (X,Y,Z) and output (F) for the logic circuit (logic function)?
methods
X
Z
Y
F

## Slide 15: truth table
n input variable ----2n row at most
X | Y | Z | F(X,Y,Z)
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
input
output
The effective output values may less than 2n, that means some inputs are invaluable.

## Slide 16: Algebraic representation
Refer to the circuit, we can write :
F=X·Z’+Y·Z+Y’ ·Z’ OR F=(X+Y’+Z) ·(Y+Z’)
  Some definitions:
  Literal
    a variable or its complement
  product term
    X·Y·Z’，A·B’·G·G，R
  sum-of-products (SOP)
  sum term
    C+D+H’，X+X+W’
  product-of-sums (POS)
  normal term (标准项)
    X·Y·Z’, A+B+C’+D’
distributivity

## Slide 17: ☆ n-variable minterm
normal product term with n literals
Exp. 3-variable X, Y, Z
minterm
X’·Y’·Z’
X’·Y’·Z
X’·Y·Z’
X’·Y·Z
X·Y’·Z’
X·Y’·Z
X·Y·Z’
X·Y·Z
X | Y | Z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
one minterm
one binary combination
one combination only let one minterm be 1
one n-variable minterm represent one n-variable combination .
minterm designation
m0
m1
m2
m3
m4
m5
m6
m7

## Slide 18: ☆ n-variable maxterm
normal sum term with n literals
maxterm
X+Y+Z
X+Y+Z’
X+Y’+Z
X+Y’+Z’
X’+Y+Z
X’+Y+Z’
X’+Y’+Z
X’+Y’+Z’
X | Y | Z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
one maxterm
one combination only let one maxterm be 0
one binary combination
one maxterm
one n-variable maxterm also represent one n-variable combination .
maxterm designation
M0
M1
M2
M3
M4
M5
M6
M7

## Slide 19: properties of minterm and maxterm
①properties of minterm
a、所有输入组合取值中，只有一组取值能令特定的某个最小项的值为1。
b、任意两个不同最小项之积为0，mi×mj=0 i≠j
c、全部最小项之和为1，
②properties of maxterm
a、所有输入组合取值中，只有一组取值能令特定的某个最大项的值为0。
b、任意两个不同最大项之和为1， Mi+Mj=1 i≠j
c、全部最大项之积为0，
③ 编号相同的最小项和最大项互为反函数
mi=(Mi)’， Mj=(mj)’

## Slide 20: ☆ canonical sum - construct an AND-OR circuit
sum of minterms
  corresponding to input combination for which the function produces a 1 output.
Exp.
F=？
=X’·Y’·Z’+X’·Y·Z+X·Y’·Z’
+X·Y·Z’+X·Y·Z
=ΣX,Y,Z(0, 3, 4, 6, 7)
X | Y | Z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
input
output
minterm list
or =m0+m3+m4+m6+m7
AND-OR

## Slide 21: ☆ canonical product - construct an OR-AND circuit
product of maxterms
  corresponding to input combination for which the function produces a 0 output.
Exp.
F=(X+Y+Z’)·(X+Y’+Z)·(X’+Y+Z’)
=∏X,Y,Z(1,2,5)
or
=M1·M2·M5
X | Y | Z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
maxterm list
OR-AND

## Slide 22: Conversion between maxterm list and minterm list
∴若已知标准和，则集合{0,…,2n-1}中剩下的编号就可以构建标准积；反之亦然。
例：∑XYZ（0、2、3、5）=∏XYZ（1、4、6、7）
n variable logic function
minterm list
k terms
maxterm list
j terms
k minterm numbers
j maxterm numbers
Complement subset of the 2n numbers
k+j=2n

## Slide 23
inverse function of a canonical logic expression：
  A canonical sum: F=…+mi+mj+… i≠j
  Its inverse function is:
    F’=…· Mi · Mj · … i≠j, vice versa.
Representation of a logic function
  ① circuit
  ② truth table
  ③ equation
    canonical sum , canonical product, and uncanonical algebra representation
  ④ number list
    minterm list, maxterm list
  ⑤ word description,…

## Slide 24: 4.2 Combinational-Circuit Analysis
Algebraic representation: F=f(A,B,C)
verify that circuit is combinational.
fill the truth table
A | B | C | F
0 | 0 | 0 | 1
… | … | … | …
1 | 1 | 1 | 0
Canonical sum or product
Minimizing the equation
write the algebraic representation according to the circuit directly
timing diagram
A
B
C
F
……
A
B
C
F

## Slide 25: Analyzing example
X | Y | Z
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
F=ΣX,Y,Z(1,2,5,7)=X’·Y’·Z+X’·Y·Z’+X·Y’·Z+X·Y·Z
OR
F=ΠX,Y,Z(0,3,4,6) =(X+Y+Z)·(X+Y’+Z’)·(X’+Y+Z)·(X’+Y’+Z)
F
0
1
1
0
0
1
0
1
Input
Output
Single direction, it’s a combinational circuit
F=1

## Slide 26: Other analysis
Minimizing the expression
F=ΣX,Y,Z(1,2,5,7)
=X’·Y’·Z+X’·Y·Z’+X·Y’·Z+X·Y·Z
=X·Z+Y’·Z+X’·Y·Z’
OR
F=ΠX,Y,Z(0,3,4,6)
=(X+Y+Z)·(X+Y’+Z’)·(X’+Y+Z)·(X’+Y’+Z)
=(Y+Z)·(X’+Z)·(X+Y’+Z’)
Write the logic expression according to the circuit
F=((X+Y’)·Z)+X’·Y·Z’

## Slide 27: Two-level structure of logic circuit
Two types
Manipulated by
De’Morgan theorem
“AND — OR”
“NAND — NAND”
“OR — AND”
“NOR — NOR”
implement sum-of products expression
implement product-of sums expression

## Slide 28: “AND-OR” and “NAND-NAND”
AND — OR
NAND — NAND
first-level
second-level

## Slide 29: “OR-AND” and “NOR-NOR”
OR-AND
NOR-NOR
first-level
second-level

## Slide 30: Timing diagram

## Slide 31: 4.3 Combinational-Circuit Synthesis
Synthesis requirements：
  analyze the word description, make sure that it could be implemented by combinational-circuit；
  Find all input and output variable ；
  Use truth table to represent the input-output logic relation；
  Use karnaugh-map to minimize the logic expression；
  Give the logic circuit diagram
?
Logic function
…
input ?
output ?
…

## Slide 32: 1、circuit descriptions and designs
Exp1：design a 4-bit prime-number detector.
F
0
1
1
1
0
1
0
1
4-bit
Prime-number detector
4-bit binary number
N3N2N1N0
Yes or No
Yes: F=1 No: F=0
N3 | N2 | N1 | N0
0 | 0 | 0 | 0
0 | 0 | 0 | 1
0 | 0 | 1 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 0 | 1
0 | 1 | 1 | 0
0 | 1 | 1 | 1
N3 | N2 | N1 | N0
1 | 0 | 0 | 0
1 | 0 | 0 | 1
1 | 0 | 1 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 0
1 | 1 | 1 | 1
F=ΣN3,N2,N1,N0 (1,2,3,5,7,11,13)
F
0
0
0
1
0
1
0
0

## Slide 33: Exp2：alarm circuit—
alarm circuit
WINDOW
DOOR
GARAGE
ALARM
PANIC
1
ENABLE
1
EXITING
0
SECURE
no
SECURE=WINDOW·DOOR·GARAGE
ALARM=PANIC+EN·EXT’ ·SEC’
ALARM=PANIC+EN·EXT’ ·(W·D·G)’

## Slide 34: 3、combinational-circuit minimization
Whether canonical sum (or product) is the final expression or not?
no
yes
Then the circuit is final result.
Need to be minimized
Obtain the minimized expression
Is the expression simplified further more?
How do I know whether the simplest circuit is done?

## Slide 35: Minimizing methods
Minimizing by switching algebra
Minimizing by karnaugh map
Minimization methods (base on two-level structure)
  Minimizing the number of first-level gates
  Minimizing the number of inputs on each first-level gates
    Basing on：T10、T10’
    X·Y+X·Y’=X；(X+Y)·(X+Y’)=X

## Slide 36: 4、Karnaugh Map
graphical representation of a logic function’s truth table .
①structure
n-variable k-map has 2n cells.
1-var k-map
2-var k-map
F（X，Y）
F
X
0
1
0
1
F
X
0
1
0
1
Y
0
1
2
3
each cell has a number which correspond to a minterm number in a truth table.
input
output

## Slide 37
3-var k-map
F（X，Y，Z）
4-var k-map
F（W, X, Y, Z）
F
XY
00
01
0
1
Z
0
1
2
3
11
10
6
7
4
5
Z
X
Y
F
WX
00
01
0
1
YZ
4
5
11
10
12
13
8
9
3
2
7
6
15
14
11
10
00
01
11
10
W
Y
X
Z
XY is arranged in Gray code.
the contents of the cells are output-value corresponding to each input combination
The bracket represents that a variable is 1 in the column cells or in row cells

## Slide 38: ② fill in the k-map for a given truth table
Copy 1s and 0s from the truth table to the corresponding cells of the map.
Exp：
truth table k-map？
X | Y | Z | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1
F
X Y
Z
1
1
0
1
0
0
1
0
00
01
11
10
X
Y
0
1
Z

## Slide 39: fill in the k-map for a given number list
F=∑X,Y,Z（1,3,4,6）
F=ΠX,Y,Z(3,5,6)
F
X Y
Z
0
0
1
1
1
1
0
0
00
01
11
10
X
Y
0
1
Z
F
X Y
Z
0
1
0
1
1
0
1
1
00
01
11
10
X
Y
0
1
Z
Order of the variables is related with the cell’s number (minterm’s number)

## Slide 40: 5、minimizing sums of products
base on：T10、T10’
X·Y+X·Y’=X (X+Y)·(X+Y’)=X
combine two adjacent “1” cell into a product term and eliminate one literal.
X | Y | Z | F
0 | 0 | 0 | 1
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
1 | 1 | 1 | 1
F=X’·Y’·Z’+X’·Y’·Z+X·Y·Z’+X·Y·Z
=X’·Y’·(Z’+Z)+X·Y·(Z’+Z)
=X’·Y’+X·Y
F
X Y
Z
0
1
0
1
0
1
0
1
00
01
11
10
X
Y
0
1
Z

## Slide 41: （1）adjacent (wrapround)
F
XY
00
01
Z
0
1
11
10
Z
X
Y
F
WX
00
01
YZ
11
10
00
01
11
10
W
Y
X
Z
adjacent
adjacent
adjacent
adjacent
input combinations of adjacent cells only differ in one variable，that is also called wrapround.

## Slide 42: （2）methods of minimization
circle 2i adjacent “1”cells, it will be a new product term with (n-i) literals.
the circle must be promised the biggest one, if enlarge the circle, then “0”cell may be included。
the combined product term is called prime implicant，PI。
1
0
0
1
1
0
1
0
00
01
11
10
F
1
0
1
0
1
1
0
0
W X
Y Z
00
01
11
W
Y
Z
10
X
1
0
0
1
1
0
1
0
00
01
11
10
1
0
1
0
1
1
0
0
W X
Y Z
00
01
11
W
Y
Z
10
X
Not the biggest circle

## Slide 43: derive prime implicant (product term)
in areas covered by the circle
1
0
0
1
1
0
1
0
00
01
11
10
F
1
0
1
0
1
1
0
0
W X
Y Z
00
01
11
W
Y
Z
10
X
① a variable is 0, then it is complemented in the product term.
② a variable is 1, then it is uncomplemented in the product term.
③a variable is 0 as well as area where it is 1, then it isn’t appear .
W=0, Z=0  W’ ·Z’
X=1 X
Y=1 & Y=0
So, this term is W’ ·X·Z’

## Slide 44: Exp
1
0
0
1
1
0
1
0
00
01
11
10
F
1
0
1
0
1
1
0
0
W X
Y Z
00
01
11
W
Y
Z
10
X
W·X’
X’·Y’·Z
W’·X·Z’
W·Y·Z
The circle more big, the variable disappeared more.
F= X’Y’Z+ W’XZ’+ WYZ+ WX’
complete sum— sum of all prime implicants.

## Slide 45: minimal sum
Complete sum may not the minimal sum, so
find the distinguished “1” cell
make sure the Essential Prime Implicant, EPI
minimal sum is the sum of EPI.

## Slide 46
1
0
0
1
1
0
1
0
00
01
11
10
F
1
0
1
0
1
1
0
0
W X
Y Z
00
01
11
W
Y
Z
10
X
distinguished “1” cell
For this example,
complete sum = minimal sum
F= X’Y’Z+ W’XZ’+ WYZ+ WX’

## Slide 47
Exp1：
1
1
1
1
0
1
1
0
0
1
1
0
0
0
0
0
00
01
11
10
F
W X
Y Z
00
01
11
W
Y
Z
X
complete sum：F=Y’Z+XZ’+XY’
minimal sum：F=Y’Z+XZ’

## Slide 48
F
AB
C
00
01
11
10
A
B
0
1
C
Exp2：derive the simplest minimal sum by k-map.
F=AC’+A’C+B’C+BC’
F
AB
C
1
0
1
1
1
1
1
0
00
01
11
10
A
B
0
1
C
rules：
按照表达式中出现的变量个数，画好方格图；
再由每个积项确定方格图中的质蕴含项(由积项中出现的变量因子对应于图中的区域的交叉部分填入“1”即可。)

## Slide 49: Continue Exp.2
F
AB
C
1
1
1
1
1
1
00
01
11
10
A
B
0
1
C
There are two results for this exp..
They have same number of product terms and each term has same literals.
A “AND-OR” logic function maybe have more than one minimal sum.
Another answer ?

## Slide 50: Exp3. minimize the logic equation
F=A’·B’·C’·D+A’·B·D’+A·C·D+A·B’+A’ ·B’ ·C’ ·D’, represent it by k-map.
solution：F=？
00
01
11
10
F
1
0
0
1
1
0
1
1
1
0
1
0
1
1
0
0
AB
CD
00
01
11
A
C
D
B
10

## Slide 51: Combinational circuit design example
Exp1：design the simplest logic circuit of the 4-bit prime-number detector.
F=∑N3N2N1N0（1，2，3，5，7，11，13）
1
F
N3N2
00
01
1
N1N0
1
11
10
1
1
1
1
00
01
11
10
N3
N1
N2
N0
minimal sum:
F=N3’·N0+N2·N1’·N0+N2’·N1·N0+N3’·N2’·N1

## Slide 52: Combinational circuit design example
Exp.2：design a 3-bit Gray code → binary code decoder.
Solution: set Gray code : G2G1G0 ,
binary code: B2B1B0
G2 | G1 | G0 | B2 | B1 | B0
0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 0 | 1
B1
G2G1
G0
G0
G2
G1
B1=G2’ ·G1+G2·G1’
0 | 1 | 0 | 1
1 | 0 | 1 | 0
B0
G2G1
G0
G0
G2
G1
B0=G2’ ·G1’ ·G0
+G2’ ·G1·G0’
+G2·G1·G0
+G2·G1’ ·G0’
0 | 0 | 1 | 1
0 | 0 | 1 | 1
B2
G2G1
G0
G0
G2
G1
B2=G2

## Slide 53: Combinational circuit design example
Exp3：design a 3-bit majority-rule circuit, that means the output value is as same as the most of input bits.
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 0
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
0 | 0 | 1 | 0
0 | 1 | 1 | 1
F
AB
C
C
A
B
F=A·B+B·C+A·C

## Slide 54: Combinational circuit design example
Exp.4：A temperature detector have four sensors settled properly in a room. When two or more sensors output high level, the detector output 1 ,otherwise output 0.
Exp.5：finish the following operation by using k-map.
Known F1=BC’+C’D’+B’CD and F2=AD’+CD+A’B’C’，do FA=F1·F2，FB=F1+F2。

## Slide 55: （3）k-map more than 4-variable
5-variable，32 cells，let variables are V、W、X、Y、Z
0 | 4 | 12 | 8 | 24 | 28 | 20 | 16
1 | 5 | 13 | 9 | 25 | 29 | 21 | 17
3 | 7 | 15 | 11 | 27 | 31 | 23 | 19
2 | 6 | 14 | 10 | 26 | 30 | 22 | 18
F
VWX
YZ
000
001
011
010
110
111
101
100
00
01
11
10
Z
Y
V
W
X
Number of cell
Arrange In Gray code
adjacent

## Slide 56: Dividing into two part
According to Shannon’s expansion theorems
9
13
5
1
8
12
4
0
00
01
11
10
F1
10
14
6
2
11
15
7
3
WX
YZ
00
01
11
W
Y
Z
X
10
V=0
25
29
21
17
24
28
20
16
00
01
11
10
F2
26
30
22
18
27
31
23
19
WX
YZ
00
01
11
W
Y
Z
X
10
V=1
F1=V’ ·F(0,W,X,Y,Z)
F2=V ·F(1,W,X,Y,Z)

## Slide 57: Exp.
find the minimal sum of the following function
F=∑V,W,X,Y,Z（7,8,9,10,11,12,23,24,26,28）
1
1
1
1
1
1
W X
Y Z
W
Y
Z
X
V=0
1
1
1
1
W X
Y Z
W
Y
Z
X
V=1

## Slide 58: 6、minimizing “product-of-sums”
Combining adjacent 2i “0”cell, get a new sum term with (n-i) literals.
or derive the minimal sum F’∑ of the inverse function first；then complement the F’∑, so the minimal product F∏ could be derived.
Exp.
00
01
11
10
F
1
1
1
1
0
1
1
0
0
0
1
0
1
1
1
0
W X
Y Z
00
01
11
W
Y
Z
X
10
F’=WYZ’+W’YX’+X’Z’
F=(W’+Y’+Z)·(W+X+Y’)·(X+Z)

## Slide 59: 7、“don’t-care” input combinations
The output doesn’t matter for certain input combination (maybe never occur in normal condition). These are called don’t care terms.
Use symbol “d”、“×”、“ Φ” to represent the output value.
In minimization, don’t care term could be used as “1” or “0” if necessary.

## Slide 60
Exp.1
00
01
11
10
F
1
d
1
1
0
d
0
0
0
0
d
1
1
0
0
0
AB
CD
00
01
11
A
C
D
B
10
F=C’·D+A·B’·D+A’·C·D
No use, no circle

## Slide 61
Exp.2：a BCD prime-number detector.
0000~1001: valid input BCD; 1010~1111: invalid input, so output don’t care。
BCD prime-number detector
BCD input
Result
Yes: F=1
No: F=0
F
N3N2
N1N0
N3
N1
N2
N0
1
1
d
d
1
1
1
d
d
d
d
F=N3’·N0+N2’·N1
4

## Slide 62
Exp.3：minimizing the following expression to minimal sum and “NAND-NAND” representation.
F=A’·B’·C’+A’·B·D’+A’·C·D+A·B·C
A·B’+A·C’=0 (约束项)
约束无关项—输入变量的取值组合受到约束，这些输入组合对应的输出也是任意的。
  即，使得约束项等于1的输入取值不可能出现。
  That means: ABCD=10×× and ABCD=1×0× never appear on the input.

## Slide 63
d
d
1
d
d
1
1
F
d
1
1
d
1
1
1
A B
C D
A
C
D
B
A·C’
A·B’
Restricted terms: A·C’, A·B’.
Also be treated as don’t-care input combinations.
the k-map
minimization
d
d
1
d
d
1
1
F
d
1
1
d
1
1
1
A B
C D
A
C
D
B

## Slide 64: 8、multiple-output minimization
using common terms adequately.
Exp：F=∑XYZ(3,6,7), G=∑XYZ(0,1,3), derive the circuit.：
(1) synthesis individually
F
X Y
Z
0
1
1
0
0
1
0
0
00
01
11
10
X
Y
0
1
Z
G
X Y
Z
0
0
1
1
0
0
0
1
00
01
11
10
X
Y
0
1
Z
F=X·Y+Y·Z
G=X’·Y’+X’·Z

## Slide 65: (2) circle the common terms in multiple-output K-maps
Algorithm
①find the m-product function of all output.
②circle the m-product’s EPI. (the common part)
③find the EPI in the leaving “1”cell.
④combining step②、③, get the final circuit.
F·G
X Y
Z
0
0
1
0
0
0
0
0
00
01
11
10
X
Y
0
1
Z
X’·Y·Z

## Slide 66
F
X Y
Z
0
1
1
0
0
1
0
0
00
01
11
10
X
Y
0
1
Z
G
X Y
Z
0
0
1
1
0
0
0
1
00
01
11
10
X
Y
0
1
Z
F·G
X Y
Z
0
0
1
0
0
0
0
0
00
01
11
10
X
Y
0
1
Z
X’·Y·Z
F=X·Y+X’·Y·Z
G=X’·Y’+X’·Y·Z
重新划出主质蕴含项
The overall product terms is reduced.

## Slide 67
列表法
 | 主蕴含项 | 最小项 |  |  |  | 
 |  | 0 | 1 | 3 | 6 | 7
F | {3 ,7} |  |  | √ |  | √
 | {6 ,7} |  |  |  | √ | √
G | {0 ,1} | √ | √ |  |  | 
 | {1 ,3} |  | √ | √ |  | 

## Slide 68: 4.5 Timing Hazards
A Static Hazard is defined when a single variable change at the input causes a momentary change in another variable [the output].
A Dynamic Hazard occurs when a change in the input causes multiple changes in the output.
keywords：glitch、hazard
reason: delay
Static Hazard: static-1, static-0 hazards

## Slide 69: 1、static hazards
①static—1 hazards
definition：a pair of input combination
（a）differ in only one variable
（b）both output 1
when this differing input change ,a momentary 0 output maybe occurred.
Exp：F=X·Z’+Y·Z，assume each gate has the same propagation delay.

## Slide 70
F
X Y
Z
0
1
1
0
1
1
0
0
00
01
11
10
X
Y
0
1
Z
X
Y
Z
Z’
X·Z’
Y·Z
F
1
0
0
1
0 glitch
F=X·Z’+Y·Z
Static-1 hazards occur in SOP implementations.
when X·Y·Z=111 → 110
Propagation delay

## Slide 71
② static—0 hazards
definition：a pair of input combination
（a）differ in only one variable
（b）both output 0
when the input change ,a momentary 1 output maybe occurred.
Exp： F=(X+Z)·(Y+Z’)
when 000 → 001

## Slide 72
F
X Y
Z
0
1
1
0
1
1
0
0
00
01
11
10
X
Y
0
1
Z
Y+Z’
X+Z
F=(X+Z)·(Y+Z’)
X
0
Y
0
Z
Z’
F
1 glitch
Static 0 hazards occur in 'Product-Of-Sums' [POS] implementations.

## Slide 73: 2、finding static hazards
（1）substitution methods
in a logic function，keep a variable unchanged，and substitute 0 or 1 for other variables, if the function can be minimized to：
  F=Xi+Xi’ ，then static-1 hazard may be exist when X is changed.
  F=Xi · Xi’ , then static-0 hazard may be exist when X is changed.

## Slide 74: (2) using k-map
若主质蕴含项（EPI）之间存在相切的部分，则电路可能存在静态冒险。
00
01
11
10
F
0
0
1
1
1
1
1
1
0
0
0
0
0
0
1
1
A B
C D
00
01
11
A
C
D
B
10
C’·D’
A’·D

## Slide 75: (3) eliminate the static hazards
00
01
11
10
F
0
0
1
1
1
1
1
1
0
0
0
0
0
0
1
1
A B
C D
00
01
11
A
C
D
B
10
C’·D’
A·D
引入一致项（consensus，冗余项）：将相切的部分划入一个质蕴含项。
A’·C’
得 F=A’·D+C’·D’+A’·C’

## Slide 76
F
X Y
Z
0
1
1
0
1
1
0
0
00
01
11
10
X
Y
0
1
Z
X
Y
Z
Z’
XZ’
YZ
F
1
0
0
1
XY
1
1
F=X·Z’+Y·Z+X·Y

## Slide 77: 第四章小结
开关代数
掌握开关代数的公理、定理。熟练应用于逻辑电路的分析和设计中。
摩根定理、广义摩根定理（反演定理）、对偶定理。
掌握逻辑函数的表示法—真值表、标准和、标准积，及最小项、最大项的定义和性质。

## Slide 78: 组合逻辑电路的分析
能写出电路的逻辑表达式。
能化简表达式（代数法、卡诺图法）
能作电路结构的变换（“与—或”转“与非—与非”，“或—与”转“或非—或非”）
能对原电路作是否存在“冒险”的判断
能画出正确的时序图。

## Slide 79
组合逻辑电路的综合
综合运用所学知识（过去所学的课程）分析、理解设计要求。
将分析所得的输入变量、输出变量及二者间的逻辑关系列入真值表。
化简，画电路
对多输出的处理—一般以各自独立输出方式求解。

## Slide 80
定时冒险
掌握冒险可能出现的情况：“与—或”结构可能出现静态—1冒险；“或—与”结构可能出现静态—0冒险。
判断电路中可能出现冒险的地方

## Slide 81: Exp.
分析如下电路
根据电路图写出逻辑表达式，判断原电路是否存在冒险。
写出最小积之和式.
若输入信号为以下顺序，无输入延迟时，请画出输出波形。
F
A
B
C
D
A
B
C
F
①
②
③
④
⑤
⑥
⑦
D

## Slide 82
试设计一个电路，当输入的4位二进制数能被2整除时，输出Y=1，当输入数能被3整除时，输出Z=1，不满足上述条件时，输出为0。