## Slide 1: Chapter 6 Combinational Logic Design Practices
MSI building blocks are the important element of combinational circuits.

## Slide 2: exercises
Part 1: 6.9, 6.20, 6.21, 6.22,
6.38, 6.43, 6.50, 6.51,
Part 2: 6.24, 6.27, 6.52, 6.53, 6.63, 6.74(use circuit to realize)

## Slide 3: Emphasis of this chapter
the function of MSIs in this chapter.
Understand the decoder and Multiplexer’s internal structure, and use them to implement logic function with necessary gates.
Be able to analyze and synthesis combinational circuit with MSIs.

## Slide 4: 6.1 Documentation Standard
1. Signal Names and Active Levels
  A better signal name indicates certain meaning, controlling, condition, data and address…
Most signals (signal name) have active level.
  active high
  active low
Active level for pins
  suffix “_L” attaching to signal name represent active low level.
    Such as, EN_L、READY_L……
    In logic relation, EN_L=EN’， READY_L=READY’。

## Slide 5: 2. logic symbols and active levels
EN
EN_L
Din
start
Dout
flg
start_L
Din
Dout
flg_L
Inversion bubble
Active low
EN
EN
Din
start
Dout
flg
start
Din
Dout
flg
Active hign
input
output

## Slide 6
Exp2：a clock gating circuit, if
①EN=1 (active high), clock signal can be transferred
②EN=0 (active low), clock signal can be transferred
EN
CLK
EN_L
CLK

## Slide 7: 3. bubble-to-bubble logic design
Make the logic circuit easier to understand.
Exp：
Not match
A
B
SEL
DATA
A
B
ASEL
DATA
match

## Slide 8: SSI ICs
74××00
74××04
package
……

## Slide 9: 6.3 Combinational PLDs
1. Programmable logic arrays (PLA)
  two level “AND—OR” device.
  Can be programmed to implement any sum-of-products logic expression.
An n×m PLA with p product terms:
  n—inputs
  m—outputs (number of OR gates)
  p—product terms (number of AND gates)

## Slide 10
4×3 with 6 product terms
AND array
OR array
fuse

## Slide 12: 2. Programmable Array Logic Devices
Fixed OR array，programmable AND array
Bidirectional input/output pins，熔丝型
PAL16L8，
Output enable

## Slide 13: 3. Generic Array Logic Devices（GAL）
an innovation of the PAL;
can be erased and reprogrammed;

## Slide 14: Classification of Combinational Logic
Combinational Logic Circuit
Arithmatic & Logical Function
Data Transmission
Code Converters
Adders
Subtractors
Comparitors
PLD’s
Multiplexers
Demultiplexers
Encoders
Decoders
Binary
BCD
7-segment

## Slide 15: 6.4 Decoder
An important type of combinational circuit .
input code word
enable input
Output code word
decoder
1-to-1
mapping
n<m
n-bit
m-bit
1-out-of-m code

## Slide 16: 1、binary decoders (n-bit → 2n-bit)
2-4 decoder（2-22）
I1
I0
Y3
Y2
Y1
Y0
truth table：？
Yi：？
I1 | I0 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0 | 0
Yi=mi
Y0=I1’·I0’ Y1=I1’·I0
Y2=I1·I0’ Y3=I1·I0
2-4
decoder
One input combination (minterm) chooses only one output.

## Slide 17: 2-4 decoder with enable input
EN | I1 | I0 | Y3 | Y2 | Y1 | Y0
0 | × | × | 0 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 0
1 | 1 | 1 | 1 | 0 | 0 | 0
I1
I0
Y3
Y2
Y1
Y0
EN
2-4
decoder
Yi=EN· mi
About the ‘EN’:
When the enable inputs are deasserted, the outputs all take on a default value.  The default is usually 0 if the outputs are asserted high and 1 if they are asserted low.

## Slide 18: MSI decoder: 74×139 , dual 2-4 decoder
EN
Input code：B（MSB）
A（LSB）
  Also be called address input.
Output code：Y3_L~Y0_L

## Slide 19: 74××138, 3-8 decoder
Enable input
EN=G1·G2A_L’·G2B_L’
Input code：
C（MSB）、B、 A
Output code：
Y0_L ~Y7_L
Yi_L=（EN·mi）’
Y0_L
Y1_L
Y2_L
Y3_L
Y4_L
Y5_L
Y6_L
Y7_L
G1
G2A_L
G2B_L
EN

## Slide 20
EN
msb
lsb

## Slide 21: Application: 3-8 decoder in memory address decoding

## Slide 22: 2. Cascading binary decoders
How to construct a 4-16、5-32 …… decoder？
use multiple 2-4 or 3-8 MSI decoders to cascade.
Design notes：
the number of MSI decoders ?
  according to the input and output bits.
only one chip output active level when a binary code data input

## Slide 23: Exp：a 4-16 decoder
Inputs: 4-bit N3、N2、N1、N0。
Outputs: 16-bit DEC15_L~DEC0_L
Need 2 pieces of 3-8 decoders.
Use the MSB of the inputs as chip-select bit.
0000 0001
0111
…
1000 1001
…
1111
N3 N2 N1 N0
N3 N2 N1 N0
output
DEC0_L
DEC1_L
DEC7_L
…
output
DEC8_L
DEC9_L
DEC15_L
…

## Slide 24
Chip selecting

## Slide 25: 3. implement canonical sum with decoder ☆
review：canonical sum
Decoder output：Yi_L=(EN·mi)’
  when EN=1， Yi_L=mi’ =Mi
How to implement canonical sum
  add an NAND gate to the decoder’s output.
Exp: (1) F=∑AB（0、3）
F=A’·B’+A·B
Enable asserted
U1A
74HC139
1Y0
4
1Y1
5
1Y2
6
1Y3
7
1A
2
1B
3
1G
1
R1
1k
A
B
F
GND
U2A
74HC00
Be viewed as a Minterm generator

## Slide 26
Exp: （2）if a 3-bit number XYZ is odd number，then F output 1，else output 0. realize the function with decoder and gates.
solution：F=？
F=ΣXYZ（1，3，5，7）
U2A
74HC20
F
1k
VCC
5V
GND
X
Y
Z
U1
74HC138
Y0
15
Y1
14
Y2
13
Y3
12
Y4
11
Y5
10
Y6
9
Y7
7
A
1
B
2
C
3
G1
6
G2A
4
G2B
5

## Slide 27
Exp: （3）F=∏XYZ（0、1、5）
solution：
U1
74HC138
1k
VCC
5V
X
Y
Z
GND
F
U2A
74HC11
Y0
15
Y1
14
Y2
13
Y3
12
Y4
11
Y5
10
Y6
9
Y7
7
A
1
B
2
C
3
G1
6
G2A
4
G2B
5

## Slide 28
Exp：4-bit prime-number detector. Realizing it with 74×138 and some gates.
VCC
5V
R1
1k
R2
1k
GND
N2
N1
N0
GND
N3
F
U3
74HC30D_6V
U1
74HC138
Y0
15
Y1
14
Y2
13
Y3
12
Y4
11
Y5
10
Y6
9
Y7
7
A
1
B
2
C
3
G1
6
G2A
4
G2B
5
U2
74HC138
Y0
15
Y1
14
Y2
13
Y3
12
Y4
11
Y5
10
Y6
9
Y7
7
A
1
B
2
C
3
G1
6
G2A
4
G2B
5
D0
D1
D7
D8
D15
VCC

## Slide 29: 4、7-segment decoder
Classify of 7-seg displayer：
in materials:
LED（发光二极管）
LCD（液晶）
In working mode:
common-cathode (共阴极)
common-anode (共阳极)
a
f
b
c
e
g
d
dp
a
b
c
d
e
dp
f
g
gnd
gnd

## Slide 30
7-segment decoder transform the BCD code to 7-segment displaying code.
devices：
7446A、74LS47 （驱动共阳）
74LS48、 74LS49（驱动共阴）
0000~1001 are useful input codes.
1010~1111 are unused BCD code.
74LS49

## Slide 31
74LS49
U1
A
5
B
1
C
2
D
4
OA
11
OD
8
OE
6
OF
13
OC
9
OB
10
OG
12
BI
3
U2
A
B
C
D
E
F
G
CK
H
GND
VCC
R1
R6
R7
R8
R9
R10
R11

## Slide 32: 5、BCD decoder（二—十进制译码器）
Inputs: BCD
Y0
Y9
……
BCD
decoder
Output:
1-out-of 10 code
74xx42

## Slide 33: 6.5 Encoder
1、binary encoder
……
……
inputs:
1-out-of-2n
code
I0
I1
Im
(m=2n-1)
……
output:
n-bit code
(number)
Y0
Y1
Yn-1
binary encoder
an object
a code
mapping

## Slide 34: Exp. 8-3 encoder
input |  |  |  |  |  |  |  | output |  | 
I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0 | Y2 | Y1 | Y0
1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
In/out:
active high

## Slide 35: 8-3 encoder’s logic expressions and circuit
Y0=I1+I3+I5+I7
Y1=I2+I3+I6+I7
Y2=I4+I5+I6+I7
When an input code is 1-out-of-8, the correct code output for it.

## Slide 36: 2、Priority Encoder
if multiple inputs are asserted simultaneously, how to deal with?
solution：assign priority to each input from high to low.
  let I7— highest priority
  and decrease from I6 down to I0
  A2,A1,A0—encode output
  IDLE—when no input is asserted,
  IDLE=1

## Slide 37
input |  |  |  |  |  |  |  | output |  |  |  |  | 
I7 | I6 | I5 | I4 | I3 | I2 | I1 | I0 | A2 | A1 |  | A0 |  | IDLE
1 | × | × | × | × | × | × | × | 1 |  | 1 |  | 1 | 0
0 | 1 | × | × | × | × | × | × | 1 |  | 1 |  | 0 | 0
0 | 0 | 1 | × | × | × | × | × | 1 |  | 0 |  | 1 | 0
0 | 0 | 0 | 1 | × | × | × | × | 1 |  | 0 |  | 0 | 0
0 | 0 | 0 | 0 | 1 | × | × | × | 0 |  | 1 |  | 1 | 0
0 | 0 | 0 | 0 | 0 | 1 | × | × | 0 |  | 1 |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 1 | × | 0 |  | 0 |  | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 |  | 0 |  | 0 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |  | 0 |  | 0 | 1
H0=I0·I1’·I2’·I3’·I4’·I5’·I6’·I7’
H7=I7
H6=I6·I7’
H5=I5·I6’·I7’
Expressions for each asserted input in the truth table of priority encoder
H1=I1·I2’·I3’·I4’·I5’·I6’·I7’
H2=I2·I3’·I4’·I5’·I6’·I7’
H3=I3·I4’·I5’·I6’·I7’
H4=I4·I5’·I6’·I7’
IDLE=(I0+I1+I2+I3+I4+I5+I6+I7)’
=I0’·I1’·I2’·I3’·I4’·I5’·I6’·I7’
A2=H4+H5+H6+H7
A1=H2+H3+H6+H7
A0=H1+H3+H5+H7

## Slide 38: 3、74××148 Priority Encoder
EI_L
  Enable Input.
I7_L~I0_L：
  encode input，I7_L has highest priority.
A2_L~A0_L
  encode output
GS_L
  GS_L =0 when one or more of the request inputs are asserted.
EO_L
  enable output
  EO_L=0 when I7_L=I6_L=…=I1_L=1 and EI_L=0.
hign
low
priority

## Slide 39: 74××148 truth table

## Slide 40: 4、cascading priority encoder
problem：how to construct 16-4、32-5 …… priority encoder？
Connecting multiple 8-3 encoders.
note：
make sure the needed number of chips according to the inputs.
need to redesign the output circuit that could produce the correct encoding output.

## Slide 41: Example ：16-4 priority encoder
use two pieces of 74××148 U1, U2，
  U1: input E15_L~E8_L;
  U2: input E7_L~E0_L;
  and E15_L is the highest priority,
  output: D3_L~D0_L，active low;
  When one or more inputs is asserted，GS_L=0；when no input is asserted ,GS_L=1 and D3_L~D0_L=1111.

## Slide 42: 16-4 priority encoder
U1
74HC148
A0
A1
A2
GS
D4
D3
D2
D5
D6
D0
D1
EI
EO
U2
74HC148
A0
A1
A2
GS
D4
D3
D2
D5
D6
D7
D0
D1
EI
EO
U3A
74HC08
U3B
74HC08
U3C
74HC08
U3D
74HC08
D7
EN15_L
EN14_L
EN13_L
EN12_L
EN11_L
EN10_L
EN9_L
EN8_L
EN7_L
EN6_L
EN5_L
EN4_L
EN3_L
EN2_L
EN1_L
EN0_L
D0_L
D1_L
D2_L
D3_L
GS_L

## Slide 43
question：if the decoder’s outputs are active high, then how to modify the circuit?
U1
74HC148
A0
A1
A2
GS
D4
D3
D2
D5
D6
D0
D1
EI
EO
U2
74HC148
A0
A1
A2
GS
D4
D3
D2
D5
D6
D7
D0
D1
EI
EO
D7
EN15_L
EN14_L
EN13_L
EN12_L
EN11_L
EN10_L
EN9_L
EN8_L
EN7_L
EN6_L
EN5_L
EN4_L
EN3_L
EN2_L
EN1_L
EN0_L
D0
D1
D2
D3
GS
U3A
74HC08
U3B
74HC08
U3C
74HC08
U3D
74HC08

## Slide 44: 6.6 Three-state Devices
1、three-state buffers

## Slide 45
EN_L
A
OUT
EN
EN_L
A
A
OUT_L
OUT_L
Enable means:
the buffer output normal logic 0、1 when EN is asserted；
the buffer output Hi-Z when EN is negated.

## Slide 46: application
return
address of data source
…
…
…
…
1-bit party line

## Slide 47: Data fighting on the three-state parity line
generally， TPLZ 、TPHZ < TPZL 、TPZH
But, to confirm the correction in application, a control logic is adopted.
000
001
010
011
…
…
SSRC
P
Q
TPL(H)Z
TPZL(H)
…
…

## Slide 48
Logic circuit
截止时间 （停滞时间）

## Slide 49: 6.7 Multiplexer
2-to-1 MUX
S=0， Y=A
S=1，Y=B
A
B
S=0
Y=A
A
B
S=1
Y=B
Logic circuit
Y=SEL’·A+SEL·B
A
B
SEL
Y

## Slide 50: 1、structure
( MUX for short )
SEL: selecting input, choose one data source to output
Y : output
enable
select
n data source
data output
( n≤2s)
mj：SEL[j] minterm

## Slide 51: 1-bit n-1 MUX
Each output equals the selected input.
The MUX works just as a n-to-1 switch.
Let b=1,
D0
D1
Dj
Dn-1
SEL
EN
Y
…
…
S-bit

## Slide 52: Exp:4-to-1 MUX
A
B
C
D
S0
S1
0
1
1
0
1
2
3
4
output
C
S1 | S0 | output
0 | 0 | A
0 | 1 | B
1 | 0 | C
1 | 1 | D

## Slide 53: 2、MSI MUX
（1）8-to-1 MUX ，74××151
EN_L
address
Y_L
Y

## Slide 54
return

## Slide 55
（2）4-bit, 2 input MUX ，74××157
74×157
1Y
4
2Y
7
3Y
9
4Y
12
1D0
2
1D1
3
2D0
5
2D1
6
3D0
11
3D1
10
4D0
14
4D1
13
S
1
EN
15

## Slide 56
（3）2 bit, 4 input MUX，74×× 153
input |  |  |  | output | 
1G_L | 2G_L | B | A | 1Y | 2Y
0 | 0 | 0 | 0 | 1C0 | 2C0
0 | 0 | 0 | 1 | 1C1 | 2C1
0 | 0 | 1 | 0 | 1C2 | 2C2
0 | 0 | 1 | 1 | 1C3 | 2C3
0 | 1 | 0 | 0 | 1C0 | 0
0 | 1 | 0 | 1 | 1C1 | 0
0 | 1 | 1 | 0 | 1C2 | 0
0 | 1 | 1 | 1 | 1C3 | 0
1 | 0 | 0 | 0 | 0 | 2C0
1 | 0 | 0 | 1 | 0 | 2C1
1 | 0 | 1 | 0 | 0 | 2C2
1 | 0 | 1 | 1 | 0 | 2C3
1 | 1 | × | × | 0 | 0
1G_L
2G_L
74×153
1Y
4
2Y
7
9
12
1C0
2
1C1
3
1C2
5
1C3
6
2C0
11
2C1
10
2C2
14
2C3
13
B
1G
1
2G
15
A

## Slide 57: 3、Expanding MUXs
Exp1：use 74××151 to implement a 16-to-1 MUX, some gates can be used if necessary.
Chips needed：
  according to the 16 inputs, need two 74××151 chips U1 & U2.
output：
  combine two chip’s outputs (Y1&Y2) into one output (Y).
Input:
  Data input : D0~D15
  Select input : A0~A3(msb)

## Slide 58
The MSB(A3) of input act as the chip-select bit.

## Slide 59
Exp2：用74××153实现4输入，4位MUX，。
设4路输入分别是：1D[3..0]、2D[3..0]、3D[3..0]、4D[3..0]；
4位输出是：Dout[3..0]
输入选择：S1、S0
解：无需外加门，只需要合理安排输入、输出数据端口即可。

## Slide 60
Dout3
S1S0

## Slide 61: 4. Implement canonical sum with MUX (supplement)
multiple input, 1 bit MUX, the output：
when EN is asserted：
as same as the canonical sum form.
74×151’s
internal circuit
mj: minterm of the select (address) inputs.

## Slide 62: EXP. A 3-bit majority circuit
0 | 0 | 1 | 0
0 | 1 | 1 | 1
F
AB
C
C
A
B
F=∑ABC(3,5,6,7)
=A’ ·B·C+A·B’ ·C+A·B·C’+A·B·C
=m3+m5+m6+m7
=1·m3+1·m5+1·m6+1·m7
= 1·m3+1·m5+1·m6+1·m7 +0·m0+0·m1+0·m2+0·m4

## Slide 63
MUX’s data input ports correspond to the output of the truth table each other.
MUX’s address input act as the minterm generator.
according to the
minterm number
truth table:
MUX:
output value
data input port
input variable
address input

## Slide 64
X
Y
Z
F
U1
~Y
6
D0
4
D1
3
D2
2
D3
1
D4
15
D5
14
D6
13
D7
12
S0
11
S2
9
S1
10
Y
5
EN
7
GND
R1
VCC
Exp1：a circuit output 1 when its 3-bit input can be divided by 3. construct the circuit by using 74××151.
So：F=∑X,Y,Z（？）
and circuit？

## Slide 65
Exp2：if the inputs are 4-bits in Exp.1, then how to design the circuit with MUX?
Solution 1：use a 16-1 MUX to design , choose a 74××150。
F=∑WXYZ（0，3，6，9，12，15）
Solution 2：仍选用74××151，先对所求函数的卡诺图做降维处理。
预备知识：卡诺图的降维
  用一个n变量的卡诺图来处理m变量的函数（n<m），这种卡诺图被称为降维（降次）的卡诺图。它允许单元格中除了0、1、无关项外，还可包含单变量或逻辑表达式。

## Slide 66: 卡诺图的降维
卡诺图降次的过程：
  设m=n+1，在m-变量函数F(X1,X2,…,Xn,Xn+1)中选择一个“入图”的变量Xi，用剩下的n个变量构造n-变量卡诺图。原图中变量Xi取值相反所覆盖的相邻的两个单元格被合并。（这两个单元格的其余变量是相同的；在真值表中对应着两行，只有Xi是不同的，其余变量均相同。）
00
01
11
10
F
W X
Y Z
00
01
11
W
Y
Z
X
10
选择入图
将被合并

## Slide 67: 降维后的输出变量的重新表达
①从真值表观察，表中的输入变量是除Xi而外剩下的变量，新行号由他们的组合值（最小项）确定。
②若在原(n+1)变量真值表中，被合并的两行的入图变量Xi与对应的F取值相同，则新表中F=Xi,
W | X | Y | Z | F | Fnew
× | × | × | 0 | 0 | Z
× | × | × | 1 | 1 | 
W、X、Y取值相同

## Slide 68
③被合并的两行的入图变量Xi与对应的F取值相反，则新表中F=Xi’
④被合并的两行的入图变量Xi所对应的F=1，则新表中F=1
⑤被合并的两行的入图变量Xi所对应的F=0，则新表中F=0
⑥用MUX实现
(若有无关项，一般(1,d)→(1),(0,d)→(0),(d,d)→(d))
W | X | Y | Z | F | Fnew
× | × | × | 0 | 1 | Z’
× | × | × | 1 | 0 | 
W | X | Y | Z | F | Fnew
× | × | × | 0 | 1 | 1
× | × | × | 1 | 1 | 
W | X | Y | Z | F | Fnew
× | × | × | 0 | 0 | 0
× | × | × | 1 | 0 | 

## Slide 69
输入 |  |  |  | 输出
W | X | Y | Z | F
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0
输入 |  |  |  | 输出
W | X | Y | Z | F
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
新输出
F
Z’
Z
0
Z’
0
1
2
3
新编号
4
5
6
7
新编号
新输出
F
Z
0
Z’
Z

## Slide 70: 降维后的三变量真值表，用74x151实现
W | X | Y | F
0 | 0 | 0 | Z’
0 | 0 | 1 | Z
0 | 1 | 0 | 0
0 | 1 | 1 | Z’
1 | 0 | 0 | Z
1 | 0 | 1 | 0
1 | 1 | 0 | Z’
1 | 1 | 1 | Z
U1
Y
6
D0
4
D1
3
D2
2
D3
1
D4
15
D5
14
D6
13
D7
12
S0
11
S2
9
S1
10
Y
5
G
7
GND
Z’
W
X
Y
F
Z

## Slide 71: 卡诺图中降维
1
0
0
0
0
1
0
1
00
01
11
10
F
0
0
1
0
0
1
0
1
W X
Y Z
00
01
11
W
Y
Z
X
10
0
Z
Z’
Z
Z
Z’
0
Z’
W X
Fnew1
Y
W
Y
X
原4变量卡诺图
新3变量卡诺图
Y’
Y
0
Y
0
Y’
Y
Y’
W X
Fnew2
Z
W
Z
X

## Slide 72: 5.Multiplexers、Demultiplexers and Buses
demultiplexers
Din
……
2n bit parallel output
demultiplexers
…
1-bit
D0
D1
Dm
SEL
n-bit
No DeMUX chips, a binary decoder with enable input can be used as a DeMUX.

## Slide 73: Mux & demux can be used to transmit several low speed signals on a single wire.
MUX
De -MUX
…
…
SRCA
SRCB
SRCC
SRCZ
SRCSEL
BUS
DSTSEL
DSTA
DSTB
DSTC
DSTZ
MUX：transform m-bit parallel-input data into serial-output data.
DeMUX：route the bus data to 1 of m destinations.

## Slide 74
（1）MUX：parallel — serial conversion
t
0
0
8-to-1 MUX
D0
D1
D2
D3
D4
D5
D6
D7
S2
S1
S0
Y
0
0
1
1
1
1
Parallel input data
Serial data output

## Slide 76
（2）DeMUX: serial — parallel conversion
Use a 74××138 as a DeMUX.

## Slide 77: Diagram of Exp.
S2S1S0
111
110
101
100
011
010
001
000
0
1
0
1
0
1
0
1

## Slide 78: 6.8 Exclusive-OR gates and Parity circuits
1、XOR and XNOR gates
X | Y | X⊕Y | (X⊕Y)’
 |  | XOR | XNOR
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
（X⊙Y）
XOR
XNOR
记忆：异或门—相同为0，相异为1
异或非门—与异或相反
Back to comparator

## Slide 79: Properties
X⊕0=X X⊕1=X’
X⊕X=0 X⊕X’=1
X⊕Y= Y ⊕ X
X⊕Y⊕Z=(X⊕Y)⊕Z=X⊕(Y⊕Z)
Equivalent symbols
Any two signals (inputs or outputs) of an XOR or XNOR gate may be complemented without changing the resulting logic function.

## Slide 80: Feature of XOR expression (k-map)
X⊕Y⊕Z=X’·Y·Z’+X·Y’·Z’+X’·Y’·Z+X·Y·Z
W⊕X⊕Y⊕Z=W’·X’·Y’·Z+W’·X’·Y·Z’+W’·X·Y’·Z’
+W’·X·Y·Z+W·X’·Y’·Z’+W·X’·Y·Z+W·X·Y’·Z+W·X·Y·Z’
010
100
001
111
XYZ
F
X Y
Z
0
1
0
1
1
0
1
0
00
01
11
10
X
Y
0
1
Z
The number of ‘1’ contained in each input combination is an odd number.

## Slide 81: 2、parity circuits
Cascade n XOR gates to form a n+1 inputs odd-parity circuit. It means that its output 1 if an odd number of its inputs are 1.
ODD=I1⊕I2⊕……⊕In
Daisy-chain connection

## Slide 82
Complement the output of odd-parity circuit，it can works as an Even-parity which output 1 if an even number of its input are 1.
Tree structure，has faster operation speed.

## Slide 83: Parity code (奇偶校验码)(supplement)
Be composed of n-bit data + 1-bit parity bit
  Even parity code：if the number of ‘1’ included in an n-bit data is odd, then the even-parity bit should be set 1. So the total number of ‘1’ in the (n+1)-bit code data is even.
  Odd parity code：if the number of ‘1’ included in an n-bit data is even, then the odd-parity bit should be set 1. So the total number of ‘1’ in the (n+1)-bit code data is odd.

## Slide 84: Example for parity circuit
Exp： a circuit adapts odd parity, if input data is 3-bit, please give the parity-bit generator.
B2 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1
B1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1
B0 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
P | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
input
output
Circuit:
P=B2’ ·B1’ ·B0’+B2’ ·B1·B0+B2·B1’ ·B0+B2·B1·B0’
=(B2⊕B1⊕B0)’
74HC386
74HC386
74HC04
B2
B1
B0
P

## Slide 85: 3、74×280 9-bit parity generator
Generate the parity bit when a code word is stored or transmitted.
Check the parity bit when a code word is retrieved or received.
EVEN=A⊕B⊕C⊕D⊕E⊕F⊕(G⊕H⊕I)’
ODD=A⊕B⊕C⊕D⊕E⊕F⊕G⊕H⊕I

## Slide 86
1
data
buffer
data
PIN
memory
WR
RD
RD
WR
POUT
ERROR
0
1
0
1
ODD=A⊕B⊕C⊕D⊕E⊕F⊕G⊕H⊕I
=PIN=POUT
2
EN

## Slide 87: 6.9 Comparators
Comparator
  compares two binary number and indicates whether they are equal.
Magnitude comparator
  interpret the binary number as signed or unsigned numbers and also indicate an arithmetic relationship (greater or less than).

## Slide 88: 1、structure of comparator
（1）1-bit comparator
（2）multiple-bit comparator
parallel comparator
iterative comparator
DIFF=A0⊕B0
EQ=（A0⊕B0）’
XOR\XNOR truth table

## Slide 89: Parallel comparator
Iterative comparator (serial comparator)
4-bit parallel comparator
Each of the input-bit pairs is compared simultaneously.

## Slide 90: 2. Iterative Circuit
Cascade n identical modules
CI
CO
PI
PO
PI1
PO1
C2
…
CI
CO
PI
PO
PIn-1
POn-1
Cn
Cn-1
CI
CO
PI
PO
C0
C1
PI0
PO0
boundary inputs
boundary output
cascading input
cascading output
All modules have the same function.

## Slide 91
comparator module
iterative comparator
lower speed, but be easy to expand
1
X0
Y0
EQI
EQO
X
Y
EQ1
X1
Y1
EQI
EQO
X
Y
EQ2
…
Xn-1
Yn-1
EQn
EQI
EQO
X
Y
EQI
EQO
X
Y

## Slide 92: 3. Magnitude comparators
（1）1-bit magnitude comparators
A | B | F(A>B) | F(A=B) | F(A<B)
0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
FA>B= A·B’
FA<B=A’ ·B
FA=B= A’ ·B’+A·B
A
B
FA>B
FA<B
FA=B

## Slide 93: （2） multiple-bit Magnitude comparators
2-bit ，input A[1..0]、B[1..0]
A1 | B1 | A0 | B0 | FA>B | FA=B | FA<B
0 | 1 | × | × |  |  | 1
1 | 0 | × | × | 1 |  | 
0 | 0 | 0 | 0 |  | 1 | 
0 | 0 | 0 | 1 |  |  | 1
0 | 0 | 1 | 0 | 1 |  | 
0 | 0 | 1 | 1 |  | 1 | 
1 | 1 | 0 | 0 |  | 1 | 
1 | 1 | 0 | 1 |  |  | 1
1 | 1 | 1 | 0 | 1 |  | 
1 | 1 | 1 | 1 |  | 1 | 
FA>B=A1·B1’
+A1’·B1’·A0·B0’
+A1·B1·A0·B0’
=A1·B1’
+(A1⊕B1)’ ·A0·B0’
FA=B=A1’·B1’·A0’·B0’
+A1’·B1’·A0·B0
+A1·B1·A0’·B0’
+A1·B1·A0·B0
=(A1⊕B1)’ ·(A0⊕B0)’
FA<B=A1’·B1
+A1’·B1’·A0’·B0
+A1·B1·A0’·B0
=A1’·B1
+(A1⊕B1)’ ·A0’·B0

## Slide 94
FA>B=(A1>B1)+(A1=B1)· ( A0>B0)
= A1·B1’ + (A’B’+AB)·(A1·B1’ )
FA=B=(A1=B1)·(A0=B0)
FA<B=(A1<B1)+(A1=B1)·(A0<B0)
A1 | B1 | A0 | B0 | FA>B | FA=B | FA<B
A1<B1 |  | × | × |  |  | 1
A1>B1 |  | × | × | 1 |  | 
A1=B1 |  | A0<B0 |  |  |  | 1
A1=B1 |  | A0>B0 |  | 1 |  | 
A1=B1 |  | A0=B0 |  |  | 1 | 
Pseudo-logic

## Slide 95: 4. Standard MSI magnitude comparator
74×85: 4-bit
Magnitude input:
  A[3..0], B[3..0]
Cascading input：
  ALBI、AEBI、AGBI，which are used to expanding comparator.
output：
  ALBO、AEBO、AGBO
    AGBO=(A>B)+(A=B)·AGBI
    AEBO=(A=B)·AEBI
    ALBO=(A<B)+(A=B)·ALBI

## Slide 96: Cascading magnitude comparator
in serial mode: iterative comparator
FA>B
FA=B
FA<B

## Slide 97
FX<Y
FX=Y
FX>Y
X[11..8]
Y[11..8]
X[7..4]
Y[7..4]
X[3..0]
Y[3..0]
U1
U2
U3
in parallel mode

## Slide 98: 6.10 Adders、Subtractors and ALU
Used to do binary addition and subtraction
1. Half adders and full adders
（1）half adders
X | Y | HS | CO
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
half sum：HS=X⊕Y
carry-out：CO=X·Y
HS
CO
X
Y

## Slide 99
（2）full adders
CIN | X | Y | S | CO
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
sum：S=X⊕Y⊕CIN
carry：CO=X·Y+CIN·X+CIN·Y

## Slide 100: 2、ripple adders
Use 1-bit full adder as a module to construct n-bit ripple adder.
X
Y
CIN
CO
S
X0
Y0
S0
C0
C1
X
Y
CIN
CO
S
X1
Y1
S1
X
Y
CO
S
Xn-1
Yn-1
Sn-1
C2
Cn
…
Expanding easily, but has lower speed

## Slide 101: 3、carry-lookahead adders
Parallel adders
issues：how to get the carry information early?
solution： carry-lookahead
（1）definition：
①carry generating variable：gi=xi·yi
②carry propagating variable：pi=xi+yi
③the Ci+1 carry-out：Ci+1=gi+pi·Ci
( Co=X·Y+Ci·(X+Y) )

## Slide 102
Ci+1=gi+pi·(gi-1+pi-1·(…(g0+p0·C0) …)
C0=0，
  Ci is relative to addends only
  The adder just has three level delay, which to reduce the calculating time.
（2）structure
Si=Xi⊕Yi⊕Ci
Ci+1=gi+pi·Ci
Two-level AND-OR expression
Xi-1
X0
Yi-1
Y0
…
…
C0
Carry-lookahead logic
Si
Xi
Yi
Ci

## Slide 103: MSI adders - 74×283
4-bit carry-lookahead adders
加法器的级联（P.482图6-89）

## Slide 104: Exp. 1-digit BCD adder
A[3:0]
B[3:0]
4-bit
Adder
(74×283)
S1[3:0]
Co1
Ci
Verifying
circuit
4-bit
Adder
(74×283)
Co2
S[3:0]
BCD
input
S1≤9, S=S1+0
S1>9, S=S1+6
Here, S≥10, Co=1;
So need a new carry generator
For 74×283, S1 ≤ 15, Co1=0;
S1>15, Co1=1

## Slide 105
U1
74HC283D_6V
SUM_4
10
SUM_3
13
SUM_1
4
SUM_2
1
C4
9
B4
11
A4
12
B3
15
A3
14
B2
2
A2
3
B1
6
A1
5
C0
7
U2
74HC283D_6V
SUM_4
10
SUM_3
13
SUM_1
4
SUM_2
1
C4
9
B4
11
A4
12
B3
15
A3
14
B2
2
A2
3
B1
6
A1
5
C0
7
U4
74HC138D_6V
Y0
15
Y1
14
Y2
13
Y3
12
Y4
11
Y5
10
Y6
9
Y7
7
A
1
B
2
C
3
G1
6
G2A
4
G2B
5
U5A
74HC32D_6V
U6
74HC30D_6V
GND
GND
A[3:0]
B[3:0]
GND
S[3:0]
Co

## Slide 106: 4、subtractor
Full subtractor
D=X⊕Y⊕BIN
BO=BIN·Y+BIN·X’+X’·Y
BIN | X | Y | D | BO
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 0
1 | 1 | 1 | 1 | 1
X
Y
BO
D
BIN

## Slide 107
Subtraction can be operated by using addition.
X-Y= X+(Y)2’s= X+(Y)1s’+1
so：D=X⊕Y’⊕BIN’
BO=(BIN’ ·X+BIN’ ·Y’ +X·Y’)’
D
BIN
BO
subtractor

## Slide 108: 5、MSI arithmetic and logic units
perform a number of different arithmetic and logical operations.
ALU
A
B
F
SEL
M
CIN
CO
G
P
A=B

## Slide 109: Class exercise 2
Y
X
Z
①
②
③
④
⑤
⑥
⑦
⑧
F
Please derive the minimal sum of the timing diagram.
Try to realize it with a 74xx151 chip.

## Slide 110: Class exercise 3
Try to implement such an encoder that output Gray code G2G1G0 corresponding to the input IN0~IN7. (no priority)

## Slide 111: Chapter 2
number systems
  Conversion between two different radix- number
  Binary signed number’s expression (S-M, 2’s, 1s’)
  Arithmetic operation (addition, subtraction, overflow…)
Code
  8421BCD, excess-3, 2421: feature
  Gray code : feature, conversion between binary number and gray code.

## Slide 112: Chapter 3
CMOS gates properties
  Basic concept: logic level, logic convention…
  CMOS logic: switching feature, internal structure…
Static electrical behavior
Dynamic electrical behavior
Other input and output structure
Noise margin, fan-out
Propagation delay in timing diagram
Transmission gate, three-state gate, open-drain (wire logic), schmitt-trigger input

## Slide 113: Chapter 4
Switching algebra
  Axioms and theorems
  Standard representation of logic functions
    Minterm, maxterm, canonical sum, canonical product, minterm list, maxterm list…
Combinational-circuit analysis
  Truth table
  Logic function
  Timing diagram
  Judge whether the hazard exist or not

## Slide 114: Chapter 4
Combinational-circuit synthesis
  Find the logic relationship between inputs and output.
  K-map
  Minimal sum, minimal product

## Slide 115: Chapter 6
The feature of each device
How to expanding its original function
Realize other function with these device
  Synthesize combinational circuit with 74xx138 or 74xx151…

## Slide 116
例1、用MSI器件实现3-bit 二进制码到Gray码的转换。
例2、用加法器74×283及一些恰当的器件实现1位BCD码的加法。
例3、假定某电路的工作波形如图所示，试找出其最简实现方案，用门电路实现；再用74×138和74×151实现。
输入
输出