## Slide 1: Chapter 7 sequential logic design principles
state, state variable, state machine
latches, flip-flops
analysis
synthesis

## Slide 2: homework
Part 1: 7.4, 7.6, 7.8, 7.12, 7.15, 7.17, 7.19,
Part 2: 7.21(a, b), 7.44, 7.46, 7.47, 7.52, 7.54,

## Slide 3: sequential circuit
Combinational
Logic
Inputs
Outputs
Memory units : store data
the outputs depend not only on its current inputs, but also on the past sequence of inputs, possibly arbitrarily far back in time.

## Slide 4: Some important concepts
state and state variable
  state : collection of state variable, contain all the information about the past necessary to account for the circuit’s future behaviors.
  state variable: the symbol representation of state.
finite-state machine
the states of a sequential circuit is always finite.
n state variables
2n possible states

## Slide 5: Some important concepts
clock
a clock signal is a signal used to coordinate the actions of two or more sequential units.
clocked synchronous state machine
all memories of the sequential circuit change their outputs only on a clock edge or signal level.
coordinate by signal level
H
L
coordinate by signal rising edge or falling edge

## Slide 6: 7.1 Bistable Element
Output variable：Q，Q_L，and Q_L=Q’
Two stable states:
Q=0、Q_L=1
Q=1、Q_L=0
feedback
1
2
Q is the state variable
a bistable storage element

## Slide 7: analysis with transfer characteristic
VOUT=T(VIN)
stable
meta-stable
stable
INV1
INV2
VIN
VOUT
VO1=VI2
VI1=VO2
O
1
2
VI1
VI2
VO1
VO2

## Slide 8: Stable and metastable

## Slide 9: 7.2 Latches and Flip_Flops
basic building block
be classified as S-R、D、T、J-K types
definition:
  latch：watches the circuit’s inputs continuously and can changes the outputs at any time.
  flip-flops：samples the circuit’s inputs and changes the output only when a clocking signal is changing.

## Slide 10: Exp: a kind of “assert”, “abort” button
Vcc
ok
abort
Vcc
ok
abort
1
0
·press “ok”, light turns on
·press “abort”, light turns off
“ok” button released – light stays on
“abort” button released – light stays off

## Slide 11: 1、S—R Latches
S-R latch built with NOR gates
Q=QN’=Q_L’
hold
reset
set
forbidden
1
2
the state variable Q can store 1-bit data.
S | R | Q | Q_L
0 | 0 | Last Q | lastQ_L
0 | 1 | 0 | 1
1 | 0 | 1 | 0
1 | 1 | 0 | 0
Function table
S
R
Q
Q

## Slide 12: S-R latch’s timing analysis
meta-stable

## Slide 13
R
S
Q
Vcc
ok
abort

## Slide 14: (2) minimum pulse width
the time of active level of S or R must be keeping longer than minimum pulse width, or else the latch may be go into metastable.
propagation delay is exist when a transition on S or R input produce a transition on an output signal.
S

## Slide 15: (3) characteristic equation
Q | S | R
0 | 0 | 0
0 | 0 | 1
0 | 1 | 0
0 | 1 | 1
1 | 0 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
characteristic equation for S-R latch:
Q*=S+R’ ·Q （S·R=0）
current state
next state
S=R=1, restricted combination
Q*
0
0
1
d
1
0
1
d

## Slide 16: 2、S-R latch
built with NAND gates
S_L | R_L | Q | Q_L
0 | 0 | 1 | 1
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Last Q | lastQ_L
S_L 、R_L: active low signals
S_L
R_L
Q_L
Q
S
R
Q
Q
hold
reset
set
forbidden

## Slide 17: 3、S-R latch with enable
S
C
R
Q
Q
metastable still exist
forbidden

## Slide 18: 4、D latch
保持
R
S
characteristic equation
Q*=D （C=1）
transfer data transparently
D
C
Q
Q
when C=0，the data is latched on Q .

## Slide 19: timing diagram
data transfered
data latched
if D changes during the thold and tsetup, the output may become metastable.

## Slide 20: 5、Edge-Triggered D Flip-Flops
Edge-Triggered ：output of flip-flop changes on the clock signal’s rising edge or falling edge.
positive edge （rising edge）
negative edge （falling edge）
CLOCK

## Slide 21: positive-edge-triggered D flip-flop
master-slave structure
  CLK=0，QM=D，US hold last Q；
  At the clock’s rising edge, US enable， UM hold last QM，Q=QM；
  CLK=1， UM hold last QM，so Q hold last Q。
UM
US

## Slide 22
Only at the rising edge of clock signal, D input could be transferred to Q output.
Dynamic-input indicator, meaning edge-triggered.
Negative-edge-triggered D flip-flop

## Slide 23: Others
D
CLK
Q
Q
CLR
PR
PR_L: preset
CLR_L: clear
edge-triggered D flip-flop with asynchronous inputs
Asynchronous inputs: force the output to go into a certain state with ignoring the triggering edge of clock.

## Slide 24: 6、edge-triggered D flip-flop with enable
characteristic equation ：Q*=EN·D+EN’·Q
D | EN | CLK | Q | Q_L
0 | 1 |  | 0 | 1
1 | 1 |  | 1 | 0
× | 0 |  | last Q | last Q_L
× | × | 0 | last Q | last Q_L
× | × | 1 | last Q | last Q_L

## Slide 25: frequency divider with D f-fs
input
(frequency, fin)
output
(frequency, fout)
divide-by-2 divider
D
Q
Q
CLK

## Slide 26: 7、scan flip-flop
TE=1，test operation mode，f-fs take TI data.
TE=0，normal D f-f-s，take D data.
D
CLK
Q
Q
TI
TE
Normal input
Test enable
Test input
2-1 MUX
D
CLK
Q
TE
D
TI
Q
Q_L
CLK

## Slide 28: 8、master/slave S-R Flip-Flops
S
R
C
Q
Q_L
S
C
R
Q
Q
QM
QM_L
Master
Slave
S
C
R
Q
Q
C=1, master is enabled and stores new data;
C= 0, master’s state is passed to enabled slave and slave stores the new value.
It is not edge-triggered f-fs, but pulse-triggered.
S
C
R
Q
Q
Q*=S+R’ ·Q （S·R=0）

## Slide 29: Timing diagram of S-R f-fs
C
S
R
QM
QM_L
Q
Q_L

## Slide 30: 9. master/slave J-K flip-flop
stucture
J
K
C
Q
Q_L
feedback
S
C
R
Q
Q
S
C
R
Q
Q
QM
QM_L
SM
RM
C=1，master is enabled and stores new data;
C = 0, slave is enabled and stores the data from master’s output
Master
Slave

## Slide 31: JK flip-flop timing diagram
C
J
K
QM
QM_L
Q
Q_L
SM
RM
QM
QM_L

## Slide 32: features
J | K | C | Q | Q_L
× | × | 0 | last Q | last Q_L
0 | 0 |  | last Q | last Q_L
0 | 1 |  | 0 | 1
1 | 0 |  | 1 | 0
1 | 1 |  | last Q_L | last Q
reset
set
toggle
hold
Pulse-triggered f-f-s
J
C
K
Q
Q
Characteristic equations ：
Q*=J·Q’+K’ ·Q
Eliminate the possible metastable which exist in the S-R f-fs (restricted input, S=R=1).
But, 1s catching and 0s catching are exist.
hold

## Slide 33: 1s catching
When C=1， last Q=0
JK=0×
if J changes to 1
master catches the changing, and sets QM=1
Even though J=1 occurred for a short time and J changes to 0 later, QM doesn’t change to 0, and passes 1 to slave when C=0. So Q hold 1.

## Slide 34: 0s catching
When C=1, last Q=1
There be JK=×0, even if K changes to 1 for a short time，flip-flop would catch the changing，and set Q=0. K changes to 0 later，Q hold 0.

## Slide 35: 10、Edge-triggered J-K Flip-Flop
sample the inputs and change the output state at the edge of clock。
characteristic equations：
Q*=J·Q’+K’ ·Q
eliminate the “1s catching” and “0s catching”.
J
CLK
K
Q
Q
J
CLK
K
Q
Q

## Slide 36: Timing diagram of edge-triggered J-K f-fs

## Slide 37: 11、T Flip-Flop
T: toggle
functional table
CLK | T | Q | Q*
 | 1 | 0 | 1
 | 1 | 1 | 0
 | 0 | × | hold
symbol
T
Q
Q
CLK
characteristic equation：Q*=T·Q’+T’ ·Q=T⊕Q
较为通用的符号
T
Q
Q
CLK
本教材的符号
Q*=Q’
The internal structure :
Fig 7-32

## Slide 38: Implementation
Contribute by D or J-K f-fs.
J
CLK
K
Q
Q
CLK
Q_L
Q
T
Q_L
CLK
Q
D
CLK
Q
Q
T
T
Q
Q
CLK
EN
Q
Q
CLK
T
功能等效

## Slide 39: T Flip-Flop with enable
EN=1，normal T flip-flop;
EN=0，hold the last value
EN
Q
Q
T
CLK
Q*=EN· (T⊕Q)+EN’ ·Q
大多数教材用的带使能的T触发器符号

## Slide 40: summary : latches and flip-flops
classified in structure：
  latches：S-R、D latches
  flip-flops：S-R、D、J-K、T flip-flops
classified in triggering form：
  pulse-triggered
  edge-triggered
one latch or flip-flop is a memory elements
  store one bit (0 or 1).
  it also act as a state variable
  more memory elements can be combined to store more bits which used to “remember” states in sequential circuit.

## Slide 41: summary : characteristic equation
S-R latch
D latch
D flip-flop
D flip-flop with enable
M/S S-R flip-flop
M/S J-K flip-flop
edge-triggered J-K flip-flop
T flip-flop
Q*=S+R’·Q （S·R=0）
Q*=D
Q*=D
Q*=EN·D+EN’·Q
Q*=S+R’·Q （S·R=0）
Q*=J·Q’+K’·Q
Q*=J·Q’+K’·Q
Q*=T·Q’+T’ ·Q

## Slide 42: 7.3 clocked synchronous state-machine analysis
emphases：
Basic structure
  Mealy machine
  Moore machine.
understand the function of each module
Derive
  excitation equations,
  transition/ output table and equations
  state table
  state diagram
  timing diagram, etc.

## Slide 43: 1、stucture
（1）Mealy machine
Next-state logic F
state memory clock
Output logic G
inputs
excitation
Current state
outputs
Clock signal
construct by combinational circuit, it output the excitation signal to storage element.
next state= F(current state,input)
construct by flip-flops, can store 2n state at most
construct by combinational circuit,
output= G(current state, input)
back

## Slide 44
（2）Moore machine
Next-state logic F
state memory clock
Output logic G
PS: output=G (current state)
inputs
Clock signal
excitation
Current state
outputs

## Slide 45: 2.analysis example
Output logic
state variable：Q0、Q1
excitation：D0、D1
output：MAX
Next-state logic
State memory

## Slide 46: excitation equation
D0=F（EN，Q1，Q0）
=[(EN·Q0’)’]’+[(EN’·Q0)’]’
=EN·Q0’+EN’·QO
D1=F（EN，Q1，Q0）
=EN’·Q1+EN·Q1’·Q0
+EN·Q1·Q0’

## Slide 47: transition equation
Characteristic equation of D f-fs：Q*=D
Transition equation：
Q1*=D1
= EN’·Q1+EN·Q1’·Q0+EN·Q1·Q0’
Q0*=D0
= EN·Q0’+EN’·QO
Substituting the excitation equations for D

## Slide 48: Transition table and state table
Q1Q0 | EN | 
 | 0 | 1
00 | 00 | 01
01 | 01 | 10
10 | 10 | 11
11 | 11 | 00
 | Q1*Q0* | 
Transition equation ：
Q1*= EN’·Q1+EN·Q1’·Q0+EN·Q1·Q0’
Q0*= EN·Q0’+EN’·QO
Current state S | EN | 
 | 0 | 1
A | A | B
B | B | C
C | C | D
D | D | A
 | S* | 
Transition table
State table
Assign state name to each state:
Q1Q0 S 00 A 01 B 10 C 11 D
Current state
input
Next state

## Slide 49: Output equation
MAX=EN·Q1·Q0
EN
MAX

## Slide 50: Transition/output table, state/output table
Q1Q0 | EN | 
 | 0 | 1
00 | 00，0 | 01，0
01 | 01，0 | 10，0
10 | 10，0 | 11，0
11 | 11，0 | 00，1
 | Q1*Q0*，MAX | 
S | EN | 
 | 0 | 1
A | A，0 | B，0
B | B，0 | C，0
C | C，0 | D，0
D | D，0 | A，1
 | S*，MAX | 
Transition/output table
state/output table

## Slide 51: State diagram
A
D
C
B
S | EN | 
 | 0 | 1
A | A，0 | B，0
B | B，0 | C，0
C | C，0 | D，0
D | D，0 | A，1
 | S*，MAX | 
EN=0
MAX=0
EN=1
MAX=0
EN=0
MAX=0
EN=1
MAX=0
EN=0
MAX=0
EN=1
MAX=0
EN=0
MAX=0
EN=1
MAX=1
Show the transition direction of current state
transition expression

## Slide 52
Q1Q0
State variable combination can be write in the circle directly.
00
11
10
01
EN=0
MAX=0
EN=1
MAX=0
EN=0
MAX=0
EN=1
MAX=0
EN=0
MAX=0
EN=1
MAX=0
EN=0
MAX=0
EN=1
MAX=1
FSM: Describes desired behavior of sequential circuit.

## Slide 53: Timing diagram
Note: analysis of finite-state machine should be base on the clock tick.
Before the clock tick (or active trigger level), the state is current state;
After the clock tick (or on the active trigger level), the state is next state.

## Slide 54: Analysis of Moore maching
excitation equations and transition equations are unchanged
MAXS=Q1·Q0

## Slide 55
Q1Q0 | EN |  | MAXS
 | 0 | 1 | 
00 | 00 | 01 | 0
01 | 01 | 10 | 0
10 | 10 | 11 | 0
11 | 11 | 00 | 1
 | Q1*Q0* （next state） |  | 
S | EN |  | MAXS
 | 0 | 1 | 
A | A | B | 0
B | B | C | 0
C | C | D | 0
D | D | A | 1
 | S* |  | 
transition table
independent of input values
state table

## Slide 56: state diagram
A MAXS=0
D MAXS=1
C MAXS=0
B MAXS=0
EN=0
EN=1
EN=0
EN=1
EN=0
EN=1
EN=0
EN=1
show output value inside the circle

## Slide 57: Timing diagram’s comparison

## Slide 58: state transition feature
transition expressions (input combinations) on arcs leaving a particular state must be mutually exclusive (互斥) and all inclusive（完备）.
  No two transition expressions can equal 1 for the same input combination;
  For every possible input combination, some transition expression must equal 1.
S0
I1
Si
S1
Sn
Ii
In
transition expression
…
…

## Slide 59: 3、analysis with J-K flip-flops
(1) excitation equation：
J0=K0=1
J1=K1=X⊕Q0
(2) transition equation:
Q0*=J0·Q0’+K0’·Q0=Q0’
Q1*=J1·Q1’+K1’·Q1 =X⊕Q0⊕Q1
CP
1
X
J0
K0
J1
K1
Q0
Q1
Z
J
CLK
K
Q
Q
J
CLK
K
Q
Q

## Slide 60
(3) output equation：Z=Q0·Q1
 | X |  | Z
Q1Q0 | 0 | 1 | 
00 | 01 | 11 | 0
01 | 10 | 00 | 0
10 | 11 | 01 | 0
11 | 00 | 10 | 1
 | Q1*Q0* |  | 
(4) transition/output table and state/output table
 | X |  | Z
S | 0 | 1 | 
A | B | D | 0
B | C | A | 0
C | D | B | 0
D | A | C | 1
 | S* |  | 
assign state name：
Q1Q0 S 00 A 01 B 10 C 11 D

## Slide 61: state diagram
A Z=0
D Z=1
C Z=0
B Z=0
X=0
X’
X’
X’
X
X
X
X=1
Circuit’s logic function:
2-bit up/down counter

## Slide 62: timing diagram
CP
X
Q1
Q0
Z
 | X |  | Z
Q1Q0 | 0 | 1 | 
00 | 01 | 11 | 0
01 | 10 | 00 | 0
10 | 11 | 01 | 0
11 | 00 | 10 | 1
 | Q1*Q0* |  | 

## Slide 63: Exp3：analyze the following circuit
T
Q
Q
CLK
X
CLK
Z
(1) excitation equation：
T1=X
T2=X·Q1
T1
T2
Q1
Q2
(2) transition equation：
Q1*=T1·Q1’+T1’·Q1= X·Q1’+X’·Q1
Q2*= T2·Q2’+T2’·Q2= X·Q1·Q2’+（X·Q1）’·Q2
(3) output equation：Z=X·Q1·Q2
T
Q
Q
CLK

## Slide 64: 7.4 clocked synchronous state-machine design
Construct state/output table
State minimization
State assignment
Construct transition/output table
Choose flip-flops
Construct excitation table
Deriving excitation equation
Deriving output equation
Drawing logic circuit diagram

## Slide 65: Exp1: sequence-detector design
Design a clocked synchronous state machine. if a continuous “110” sequence is included in the serial input binary numbers, the circuit output 1. synthesis by D flip-flops . that is
input P：
output C：
solution ：Moore machine
（1）input and output variable
input：P（a bit sent into the circuit）
output：C（the detecting result, 1 bit）
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
first input

## Slide 66: state analysis of exp.1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0
P：
C：
task：detect section 110
If the previous one input bit is 0, then memory as a state, S0
Input 0
Input 1
If the previous one input bit is 0, then memory as a state, S1
If the previous one input bit is 1, then memory as a state, S2
If the previous two input bit is 01, also memory as state S0
If the previous two input bit is 1, then memory as a state, S3
If the previous two input bit is 1, also memory as state S2

## Slide 67: Exp1: sequence-detector design
Defining states：
S0 — received a single 0
S1 — received a single 1
S2 — received a continuous “11”
S3— received a continuous “110”
S | P |  | C
 | 0 | 1 | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S3 | S2 | 0
S3 | S0 | S1 | 1
 | S* |  | 
state/output table

## Slide 68
（2）state minimization
（3）state assignment（状态的分配、赋值）
n state variables → 2n states。
Then, S states need (?) state variables (flip-flops) to represent.
The number of f-fs：m=2，named Q0、Q1
Assign state variable combinations to each symbol state：
S： S0 S1 S2 S3
Q1Q0： 00 01 10 11
different assignment
☟
different circuit
at least

## Slide 69: (4) construct transition/output table
substitute state combinations for the state symbols .
Q1Q0 | P |  | C
 | 0 | 1 | 
00 | 00 | 01 | 0
01 | 00 | 10 | 0
10 | 11 | 10 | 0
11 | 00 | 01 | 1
 | Q1*Q0* |  | 
S0
S1
S2
S3
S | P |  | C
 | 0 | 1 | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S3 | S2 | 0
S3 | S0 | S1 | 1
 | S* |  | 

## Slide 70: (5) Construct excitation table
Choose flip-flops and use application equation to construct excitation table.
Q1Q0 | P |  | C
 | 0 | 1 | 
00 | 00 | 01 | 0
01 | 00 | 10 | 0
10 | 11 | 10 | 0
11 | 00 | 01 | 1
 | D1D0 |  | 
Q | Q* | D
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Q | D | Q*
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Function table of D f-f-s
Application table
Excitation table
Application equation：D=Q*

## Slide 71: (6) Deduce the excitation equations
1
0
1
0
1
0
0
0
P
Q1Q0
Q1
Q0
D1
0
1
0
1
1
0
0
0
P
Q1Q0
Q1
Q0
D0
D1=Q1·Q0’+Q1’·Q0·P
D0=Q1·Q0’·P+Q1’·Q0’·P+Q1·Q0·P
Q1Q0 | P |  | C
 | 0 | 1 | 
00 | 00 | 01 | 0
01 | 00 | 10 | 0
10 | 11 | 10 | 0
11 | 00 | 01 | 1
 | D1D0 |  | 

## Slide 72: (7) Deduce the output equation
C=Q1·Q0
Q1Q0 | P |  | C
 | 0 | 1 | 
00 | 00 | 01 | 0
01 | 00 | 10 | 0
10 | 11 | 10 | 0
11 | 00 | 01 | 1
 | Q1*Q0* |  | 

## Slide 73: Circuit for exp1
U1A
74HC74D_6V
D
2
Q
5
Q
6
CLR
1
CLK
3
PR
4
U2B
74HC74D_6V
D
2
Q
5
Q
6
CLR
1
CLK
3
PR
4
D1
Q1
D0
Q0
P
C
CLK

## Slide 74: Assignment 2
S | P |  | C
 | 0 | 1 | 
S0 | S0 | S1 | 0
S1 | S0 | S2 | 0
S2 | S3 | S2 | 0
S3 | S0 | S1 | 1
 | S* |  | 
Issue: if we adapt Gray code for state assignment, then what the circuit is?
S： S0 S1 S2 S3
Q1Q0：00 01 11 10
Q1Q0 | P |  | C
 | 0 | 1 | 
00 | 00 | 01 | 0
01 | 00 | 11 | 0
11 | 10 | 11 | 0
10 | 00 | 01 | 1
 | Q1*Q0* |  | 

## Slide 75: Assignment with Gray code
Q1Q0 | P |  | C
 | 0 | 1 | 
00 | 00 | 01 | 0
01 | 00 | 11 | 0
11 | 10 | 11 | 0
10 | 00 | 01 | 1
 | D1 D0 |  | 
0
1
1
0
0
1
0
0
P
Q1Q0
Q1
Q0
D1
1
1
1
1
0
0
0
0
P
Q1Q0
Q1
Q0
D0
D0=P
D1=Q1·Q0+Q0·P

## Slide 76: Another sequence detector : use mealy machine
If a circuit’s input P receives continuous 101 binary sequence, then C output 1, otherwise C output 0. And overlap is not permitted.
（1）defining states
S0—receive a single 0，C=0
S1—receive a single 1，C=0
S2—receive continuous “10”，C=0
S3—receive continuous “101”，C=1
S | P | 
 | 0 | 1
S0 | S0，0 | S1，0
S1 | S2，0 | S1，0
S2 | S0，0 | S3，1
S3 | S0，0 | S1，0
 | S*，C | 
(2) Construct state/output table

## Slide 77: (3) State minimization
S0 and S3 are equivalent states，so eliminate S3, and get the minimized state/output table.
S | P | 
 | 0 | 1
S0 | S0，0 | S1，0
S1 | S2，0 | S1，0
S2 | S0，0 | S3，1
S3 | S0，0 | S1，0
 | S*，C | 
S0
Equivalent states: two states produce the same values at the output; and they have either the same next state or equivalent next state.（section 7.4.2）

## Slide 78: (4) State assignment
Number of f-fs：
named Q1、Q0 Q1Q0=00，01，10，11
assign 3 of the 4 binary values to the 3 known states。like， S0 — 00，S1 —01，S2 — 11 Q1Q0=10，unused state.
Q1Q0 | P | 
 | 0 | 1
00 | 00，0 | 01，0
01 | 11，0 | 01，0
11 | 00，0 | 00，1
10 | ？ | ？
 | Q1*Q0*，C | 
Transition/output table

## Slide 79: Disposition of unused states
Q1Q0 | P | 
 | 0 | 1
00 | 00，0 | 01，0
01 | 11，0 | 01，0
11 | 00，0 | 00，1
10 | 00，0 | 00，0
 | Q1*Q0*，C | 
Q1Q0 | P | 
 | 0 | 1
00 | 00，0 | 01，0
01 | 11，0 | 01，0
11 | 00，0 | 00，1
10 | dd，d | dd，d
 | Q1*Q0*，C | 
①minimal risk
②minimal cost

## Slide 80: (5) Construct excitation table
Use D f-fs and in minimal cost disposition.
Q1Q0 | P | 
 | 0 | 1
00 | 00,0 | 01,0
01 | 11,0 | 01,0
11 | 00,0 | 00,1
10 | dd,d | dd,d
 | D1D0,C | 
Excitation table
Application equation：D=Q*

## Slide 81: (6) Derive the excitation equations and output equation
D1=Q1’ ·Q0·P’
D0=P·Q1’+Q1’ ·Q0
C=Q1·P

## Slide 82: another way: synthesis using J-K f-fs
Q | Q* | J | K
0 | 0 | 0 | d
0 | 1 | 1 | d
1 | 0 | d | 1
1 | 1 | d | 0
Application table of J-K f-fs
Q1Q0 | P | 
 | 0 | 1
00 | 0d,0d,0 | 0d,1d,0
01 | 1d,d0,0 | 0d,d0,0
11 | d1,d1,0 | d1,d1,1
10 | dd,dd,d | dd,dd,d
 | J1K1,J0K0,C | 
Excitation table
Minimal cost disposition
Also for detecting continuous 101 sequence.

## Slide 83: Excitation equations and output equation
Excitation equations
J1=P’·Q0 K1=1
J0=P K0=Q1
output equation
C=Q1·P
1J
4
1Q
15
1Q
14
1K
16
1CLK
1
1J
4
1Q
15
1Q
14
1K
16
1CLK
1
P
J0
K0
J1
K1
Q0
Q1
C
VCC
clk

## Slide 84: Design examples in book
Exp1:
Design a machine inputs A and B with output Z that is 1 if:
  A had the same value at the two previous ticks
  B has been 1 since the last time the above was true ）
CLK
A
B
Z

## Slide 85: 1. Find states
电路开始工作，设置INIT状态，Z=0
状态A0，A收到一个0，……，Z=0
状态A1，A收到一个1，……，Z=0
状态OK0，A收到连续的两个0，Z=1
状态OK1，A收到连续的两个1，Z=1
状态A001，A收到连续的两个0后，收到1，同时B=1，Z=1
状态A110，A收到连续的两个1后，收到0，同时B=1，Z=1
状态AE10，A已经收到过连续的00或11，收到连续的10，同时B=1，Z=1
状态AE01，A已经收到过连续的00或11，收到连续的01，同时B=1，Z=1

## Slide 86
电路开始工作，设置INIT状态，Z=0
状态A0，A收到第一个0，Z=0
状态A1，A收到第一个1，Z=0
状态OK0，A收到连续的两个0，Z=1
状态OK1，A收到连续的两个1，Z=1
状态A001，A收到连续的两个0后，收到1，同时B=1，Z=1
状态A110，A收到连续的两个1后，收到0，同时B=1，Z=1
状态AE10，A已经收到过连续的00或11，收到连续的10，同时B=1，Z=1
状态AE01，A已经收到过连续的00或11，收到连续的01，同时B=1，Z=1
S | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
INIT | A0 | A0 | A1 | A1 | 0
A0 | OK0 | OK0 | A1 | A1 | 0
A1 | A0 | A0 | OK1 | OK1 | 0
OK0 | OK0 | OK0 | A001 | A1 | 1
OK1 | A0 | A110 | OK1 | OK1 | 1
A001 | A0 | AE10 | OK1 | OK1 | 1
A110 | OK0 | OK0 | AE01 | A1 | 1
AE10 | OK0 | OK0 | AE01 | A1 | 1
AE01 | A0 | AE10 | OK1 | OK1 | 1
 | S* |  |  |  | 

## Slide 87: State minimization
S | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
INIT | A0 | A0 | A1 | A1 | 0
A0 | OK0 | OK0 | A1 | A1 | 0
A1 | A0 | A0 | OK1 | OK1 | 0
OK0 | OK0 | OK0 | A001 | A1 | 1
OK1 | A0 | A110 | OK1 | OK1 | 1
A001 | A0 | AE10 | OK1 | OK1 | 1
A110 | OK0 | OK0 | AE01 | A1 | 1
AE10 | OK0 | OK0 | AE01 | A1 | 1
AE01 | A0 | AE10 | OK1 | OK1 | 1
 | S* |  |  |  | 
Equivalent states, eliminate state AE10
Equivalent states，eliminate state AE01

## Slide 88: State minimization
S | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
INIT | A0 | A0 | A1 | A1 | 0
A0 | OK0 | OK0 | A1 | A1 | 0
A1 | A0 | A0 | OK1 | OK1 | 0
OK0 | OK0 | OK0 | A001 | A1 | 1
OK1 | A0 | A110 | OK1 | OK1 | 1
A001 | A0 | A110 | OK1 | OK1 | 1
A110 | OK0 | OK0 | A001 | A1 | 1
 | S* |  |  |  | 
Equivalent states, eliminate state A001
Equivalent states，eliminate state A110

## Slide 89: Minimal state table
S | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
INIT | A0 | A0 | A1 | A1 | 0
A0 | OK0 | OK0 | A1 | A1 | 0
A1 | A0 | A0 | OK1 | OK1 | 0
OK0 | OK0 | OK0 | OK1 | A1 | 1
OK1 | A0 | OK0 | OK1 | OK1 | 1
 | S* |  |  |  | 

## Slide 90: State assignment
Possible state assignments
 | assignment |  |  | 
State name | Simplest Q1~Q3 | Decomposed Q1~Q3 | One-hot Q1~Q5 | Almost one-hot Q1~Q4
INIT | 000 | 000 | 00001 | 0000
A0 | 001 | 100 | 00010 | 0001
A1 | 010 | 101 | 00100 | 0010
OK0 | 011 | 110 | 01000 | 0100
OK1 | 100 | 111 | 10000 | 1000
Q1=0, in the INIT state
Q1=1, in the non-INIT state
In the non-INIT state,
Q3 give the previous value of A;
Q2 indicates that the conditions for a 1 output are satisfied in the current state.

## Slide 91: Transition/output table and excitation table
Q1Q2Q3 | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
000 | 100 | 100 | 101 | 101 | 0
100 | 110 | 110 | 101 | 101 | 0
101 | 100 | 100 | 111 | 111 | 0
110 | 110 | 110 | 111 | 101 | 1
111 | 100 | 110 | 111 | 111 | 1
 | D1 D2 D3 |  |  |  | 
Q1Q2Q3 | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
000 | 100 | 100 | 101 | 101 | 0
100 | 110 | 110 | 101 | 101 | 0
101 | 100 | 100 | 111 | 111 | 0
110 | 110 | 110 | 111 | 101 | 1
111 | 100 | 110 | 111 | 111 | 1
 | Q1*Q2*Q3* |  |  |  | 

## Slide 92: Completed excitation table
Q1Q2Q3 | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
000 | 100 | 100 | 101 | 101 | 0
001 |  |  |  |  | 
010 |  |  |  |  | 
011 |  |  |  |  | 
100 | 110 | 110 | 101 | 101 | 0
101 | 100 | 100 | 111 | 111 | 0
110 | 110 | 110 | 111 | 101 | 1
111 | 100 | 110 | 111 | 111 | 1
 | D1 D2 D3 |  |  |  | 
？
Two approaches:
Minimal cost
Minimal risk
Disposition of unused states

## Slide 93
Q1Q2Q3 | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
000 | 100 | 100 | 101 | 101 | 0
001 |  |  |  |  | 0
010 |  |  |  |  | 0
011 |  |  |  |  | 0
100 | 110 | 110 | 101 | 101 | 0
101 | 100 | 100 | 111 | 111 | 0
110 | 110 | 110 | 111 | 101 | 1
111 | 100 | 110 | 111 | 111 | 1
 | D1 D2 D3 |  |  |  | 
0
0
0
0
1
1
1
1
00
01
11
10
D1
0
0
0
0
0
0
0
0
AB
Q2Q3
00
01
11
10
Q1=0
D1
1
1
1
1
1
1
1
1
00
01
11
10
1
1
1
1
1
1
1
1
AB
Q2Q3
00
01
11
10
Q1=1
Minimal risk
D1=Q1+Q2’Q3’
D2, D3……
Z=Q1·Q2

## Slide 94
Q1Q2Q3 | A B |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
000 | 100 | 100 | 101 | 101 | 0
001 |  |  |  |  | d
010 |  |  |  |  | d
011 |  |  |  |  | d
100 | 110 | 110 | 101 | 101 | 0
101 | 100 | 100 | 111 | 111 | 0
110 | 110 | 110 | 111 | 101 | 1
111 | 100 | 110 | 111 | 111 | 1
 | D1 D2 D3 |  |  |  | 
d
d
d
d
1
1
1
1
00
01
11
10
D1
d
d
d
d
d
d
d
d
AB
Q2Q3
00
01
11
10
Q1=0
D1
1
1
1
1
1
1
1
1
00
01
11
10
1
1
1
1
1
1
1
1
AB
Q2Q3
00
01
11
10
Q1=1
Minimal cost
D1=1
D2,D3……
Z=Q2

## Slide 95: Logic diagram in minimal cost for Exp1

## Slide 96: Logic diagram in minimal risk for Exp1

## Slide 97: Exp2: 1s-counting machine
design a clocked synchronous state-machine with two inputs X and Y, and one output Z, the output should be 1 if the number of 1 inputs on X and Y since reset is a multiple of 4, and 0 otherwise.
X | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 0
Y | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1
Z |  | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
reset

## Slide 98: Naming state
Each state record the number of 1 input on X and Y：
Multiple of 4 imply that the number of 1 input can be divided by 4. (MOD 4=0)
  (N MOD 4) =0，— Z=1 —— S0
  (N MOD 4) =1，— Z=0 —— S1
  (N MOD 4) =2，— Z=0 —— S2
  (N MOD 4) =3，— Z=0 —— S3

## Slide 99: Synthesis steps
S | XY |  |  |  | Z
 | 00 | 01 | 11 | 10 | 
S0 | S0 | S1 | S2 | S1 | 1
S1 | S1 | S2 | S3 | S2 | 0
S2 | S2 | S3 | S0 | S3 | 0
S3 | S3 | S0 | S1 | S0 | 0
 | S* |  |  |  | 
1、state/output table
2、state assignment:
S0 — 00、S1 — 01、 S2 — 11、S3 — 10
3、transition/output table
……
4、application table
……
……

## Slide 100: Exp3: a combination lock
requirement:
UNLK=1 if and only if X is 0 and the sequence of inputs received on X at the preceding seven clock ticks of X was 0110111.
HINT=1 if and only if the current value of X is the correct one to move the machine closer to being in the “unlocked” state (with UNLK=1).
It is a sequence-detector machine

## Slide 101: States analysis
Input state output
Got 1 A UNLK=0, HINT=0
Got 0 B UNLK=0, HINT=1
Got 01 C UNLK=0, HINT=1
Got 011 D UNLK=0, HINT=1
Got 0110 E UNLK=0, HINT=1
Got 01101 F UNLK=0, HINT=1
Got 011011 G UNLK=0, HINT=1
Got 0110111 H UNLK=0, HINT=1
Got 01101110 I UNLK=1, HINT=1
X | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 0
UNLK | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
HINT | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1

## Slide 102: State table for combination-lock machine
Equivalent states
S | X | 
 | 0 | 1
A | B，01 | A，00
B | B，00 | C，01
C | B，00 | D，01
D | E，01 | A，00
E | B，00 | F，01
F | B，00 | G，01
G | E，01 | H，01
H | I，11 | A，00
I | B，00 | C，01
 | S*，UNLK HINT | 
S | X | 
 | 0 | 1
A | B，01 | A，00
B | B，00 | C，01
C | B，00 | D，01
D | E，01 | A，00
E | B，00 | F，01
F | B，00 | G，01
G | E，01 | H，01
H | B，11 | A，00
 | S*，UNLK HINT | 
Omit the later steps.
……

## Slide 103: 7.5 designing state machines using state diagram
Difference between state table and state diagram design：
状态表是穷举列表的方法
状态图表达状态的转移用一条带转移表达式的弧线，其中可能包含多个输入。经常不能一次达到状态转移的完备性。

## Slide 104
Exp1: a sequence-detector, if the control input A =1, and serial input B are continuous “110”, then output C =1.
S0
S1
S2
S3
S4
S
A,B/C
A’/0
A,B’/0
A,B/0
A,B/0
A,B’/1
A’/0
A’/0
A’/0
A’/0
A,B’/0
A,B/0
A,B’/0
A,B/0
A,B/0
A,B’/0

## Slide 105
Equivalent states in state diagram：
if two node’s directed arc for a given input combination point to the same nodes, then they are equivalent states.
  S0 and S1are equivalent states here。
S1
S2
S3
S4
A’+ A·B’/ 0
A,B/0
A,B/0
A,B’/1
A’/0
A’+ A·B’/0
A,B/0
A,B/0
A’+A·B’/0

## Slide 106: state assignment
construct transition/output table and derive the excitation table.
Q1Q0 | AB |  |  | 
 | 00 | 01 | 11 | 10
00 | 00，0 | 00，0 | 01，0 | 00, 0
01 | 00，0 | 00，0 | 11，0 | 00, 0
11 | 00，0 | 00，0 | 11，0 | 10, 1
10 | 00，0 | 00，0 | 01，0 | 00, 0
 | Q1*Q0*，C |  |  | 
S1
S2
S3
S4
D=Q*

## Slide 107
Q1Q0 | AB |  |  | 
 | 00 | 01 | 11 | 10
00 | 00，0 | 00，0 | 01，0 | 00, 0
01 | 00，0 | 00，0 | 11，0 | 00, 0
11 | 00，0 | 00，0 | 11，0 | 10, 1
10 | 00，0 | 00，0 | 01，0 | 00, 0
 | D1 D0，C |  |  | 
D1=A·B·Q0+A·Q1·Q0
D0=A·B
C=A·B’ ·Q1·Q0

## Slide 108: Exp2:T-bird tail lights
input：L（LEFT）、R（RIGHT）、H（HAZ）
output：LA、LB、LC、RA、RB、RC
Working condition：
  input L — LA、LB、LC lighting on successively and off
  input R — RA、RB、RC lighting on successively and off；
  input H — all lights flashing on and off in unison
  no input, all lights off.
state | description
L1 | LA on
L2 | LA、LB on
L3 | LA、LB、LC on
R1 | RA on
R2 | RA、RB on
R3 | RA、RB、RC on
LR3 | all on simultaneous
IDLE | all off
LA
LB
LC
RA
RB
RC

## Slide 109: First State diagram
IDLE
LR3
L1
L3
L2
R1
R3
R2
H=1
L=1
1
1
1
R=1
1
1
1
Some faulty aspect
……
Thinking carefully
H’L’R’
 | input |  |  | 
S | H | L | R | S*
IDLE | 1 | × | × | LR3
IDLE | × | 1 | 1 | LR3
IDLE | 0 | 1 | 0 | L1
IDLE | 0 | 0 | 1 | R1
IDLE | 0 | 0 | 0 | IDLE
1

## Slide 110: Corrected diagram
IDLE
LR3
L1
L3
L2
R1
R3
R2
H+LR
H’LR’
1
1
1
H’L’R
1
1
1
1
H’L’R’

## Slide 111: Corrected diagram again
IDLE
LR3
L1
L3
L2
R1
R3
R2
H+LR
H’LR’
H’
H’
1
H’L’R
1
H’
H’
1
H’L’R’
H
H
H
H

## Slide 112: State assignment
8 states，need 3 f--fs，so named Q0、Q1、Q2。
Assign state：
S — IDLE L1 L2 L3 R1 R2 R3 LR3
Q2Q1Q0 — 000 001 011 010 101 111 110 100
transition list :
  Each row contains the current state, next state and transition expression（p.427 table 7-14）
Derive transition equation：
  Transition list can be viewed as a sort of truth table
  Current state Q2, Q1, Q0 and transition expressions (input combinations) are input variables
  Next state Q2*, Q1*, Q0* are output variables

## Slide 113: Summary for chapter 7
Basic sequence element
  Latches
  Flip-flops
  Latches and flip-flops are used as state storage.
State machine structure
  Mealy machine
  Moore machine

## Slide 114
Important features
  Excitation signal, excitation equations
  Transition equations
  Output equations
  Transition/output table
  State/output table
  State diagram
  Timing diagram

## Slide 115: 课堂练习
已知某同步时序电路的转移方程、输出方程如下，请写出其转移/输出表，并画出状态图，试说明其功能。状态变量赋值按Q1Q0=00、01、10、11。
Q1*=X’·Q0·Q1’+X’·Q1
Q0*=X’·Q0’+X’·Q1·Q0
Y=Q0·Q1

## Slide 116: Class exercise
若某电路输入端的串行序列X是1101时，输出L=1，否则L=0。
试写出该电路的Mealy machine 和Moore machine 的状态/输出表。