## Slide 1: Chapter 8 sequential logic design practices
emphasis：
Counter:
  counter composed of flip-flops and MSI counters, sequence generator
Shift register:
  data shift function, ring counter, Johnson counter, sequence generator and detector

## Slide 2: exercises
8.13, 8.14, 8.16(starting with state 00001)
8.26, 8.35, 8.38, 8.55
8.57, 8.58,

## Slide 3: 8.1 documentation standards
In logic block, input is on the right, output is on the left.
input
output
…
…
…
…
…
…
PR
CLR
…
…
Edge-triggered
…
…
C
CLK
Pulse-triggered

## Slide 4: 8.2 latches and flip-flops
1. SSI latches and flip-flops(figure 8-3)
74×74 — dual D f-fs
74×109 — dual J-K’ f-fs
74×375 — quad D latch
2. Switch debouncing
eliminate bouncing that occurs when the mechanical switch is on and off.
3. Bus-holder
避免三态输出总线上长期无信号而由噪声、干扰等产生较大电流而损坏器件的问题。

## Slide 5: Switch debouncing
Some switch, button
A usual switch debouncer
当机械触点断开、闭合时,电压信号会抖动。抖动时间的长短由按键的机械特性决定,一般为5ms～10ms。
S_L
R_L
R_L
S_L
Q
离开B，未到A
碰到A

## Slide 6: 3. Multibit registers and latches
Collection of two or more D f-fs with a common clock input .
Cab be used to store a multiple-bit data.
with tri-state output
latch with tri-state output

## Slide 7: PLDs
16V8 (20 Pins)
can have 16 inputs (max) and/or 8 outputs (marcrocells)
has 32 inputs to each of the AND gates (product terms)
20V8 (24 pins)
can have 20 inputs (max) and/or 8 outputs (marcrocells)
has 40 inputs to each of the AND gates (product terms)
22V10 (24 pins)
can have 22 inputs and/or 10 outputs (max)
has 44 inputs to each of the AND gates
It will be slower and will more wasted silicon space
Solution? Use CPLDs

## Slide 8
GAL16V8
Each output is programmable as combinational or registered
Also has programmable output polarity
AND Plane
The OR gates
XOR gates to
make inverting or
non-inverting buffer

## Slide 9
GAL22V10
S0
S1

## Slide 10
Active low S1S0=00
Active high S1S0=01
Active low S1S0=10
Active high S1S0=11
可实现时序逻辑
可实现组合逻辑

## Slide 11: A General CPLD structure
A collection of PLDs on a single chip with
Programmble interconnects

## Slide 12: Product-term CPLD structure
LAB
(Logic Array Block)
I/O
Control
Block
PIA
(Programmable Interconnection Array)
MAX7000

## Slide 13: Macrocell structure

## Slide 14: FPGA structure
Altera’s FLEX/ACEX

## Slide 15: Macrocell structure

## Slide 16: 8.4 counters
Any sequential circuit whose state diagram is a single cycle.
Transition of successive state is unconditional.
Modulus — the number of states in the cycle
S1
Sj
Sm
S3
S2
…
…
Modulo-m counter
(m states → n=
flip-flops)
clock
n
Q[0..n-1]

## Slide 17: General types of electronic counters
Classify in counting sequence
  up counters, which count in ascending binary order
  down counters, which count in descending binary order
Classify in counter circuit
  Asynchronous (ripple) counter
  Synchronous counter
  Shift-Register Counters
    Ring counter
    Johnson counter
Application: counter, timer, frequency-division, sequence-generator, ……

## Slide 18: 1、ripple counters
CLK
Q
Q
T
Basic unit:
modulo-2 counter
0
1
1
1
CLK
Q

## Slide 19: 1、ripple counters
Q0
4-bit binary Counter output
(LSB)
CLK
Q1
Q0
Q3
Q2
CLK
Q
Q
T
Q1
Q
Q
T
Q2
Q
Q
T
Q3
(MSB)
Q
Q
T
行波计数器、
串行计数器
（是异步计数的）
(fig8-24)
CLK signal has propagation delay .
(counting carry information ripples from Q0 to Q3)

## Slide 20: 4-bit binary counter’s state diagram
0000
0001
0010
0011
0100
0101
0110
0111
1111
1110
1101
1100
1011
1010
1001
1000
It’s a up counter (or increased mode), and has 24 states.
n-bit binary counter → has n flip-flops
→2n states

## Slide 21
Issue 1：how to make a down counter by T f-fs？
Issue 2：how to make the ripple counter by using D and J-K f-fs？(as homework, 4-bit)
--------------------------------------------------------------------------Also be acted as a digital frequency divider (divided-by-2n)
divide-by-2
CLK
Q1
Q0
Q3
Q2
divide-by-4
divide-by-8
divide-by-16

## Slide 22: 2、 Synchronous counters
All flip-flops change their states at the same triggering time of a common CLK signal.
Working features： EN signal propagates serially.
EN0=CNTEN
EN1=Q0·CNTEN
EN2=Q1·EN1
EN3=Q2·EN2
transition equations： Qi*= ENi·Qi’+ENi’·Qi
EN0
EN1
EN2
EN3
(LSB)
(MSB)
synchronous counter with serial enable signal
教材fig8-25

## Slide 23: synchronous counter with parallel enable signal
(LSB)
(MSB)
EN0
EN1
EN2
EN3
CNTEN signal controls the f-fs simultaneously ;
the fastest binary counters structure.
Judge this circuit’s counting sequence (up or down)?
教材fig8-26

## Slide 24: binary synchronous counter design with D flip-flops
Exp1: design a 3-bit binary synchronous down counter ,counter output Q2(msb),Q1,Q0。
the functional table：
Q2 | Q1 | Q0 | Q2* | Q1* | Q0*
0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1
0 | 1 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 1 | 0
111
110
101
100
000
001
010
011
Q2 Q1 Q0

## Slide 25: excitation table of the counter
Q2 | Q1 | Q0 | Q2* | Q1* | Q0* | D2 | D1 | D0 | J2K2 | J1K1 | J0K0
0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1d | 1d | 1d
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0d | 0d | d1
0 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0d | d1 | 1d
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 0 | 0d | d0 | d1
1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | d1 | 1d | 1d
1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | d0 | 0d | d1
1 | 1 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | d0 | d1 | 1d
1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | d0 | d0 | d1
excitation equations：
D2=Q2Q1+Q2Q0+Q2’Q1’Q0’
D1=Q1Q0+Q1’Q0’
D0=Q0’
……

## Slide 26: design synchronous counter with module less than 2n
module of the counter m<2n，the disposition of unused state：
minimal risk
minimal cost，need to verify the unused state that assures the circuit can be returned to the normal
Need to verify the counter’ s self-correction
Exp2：design a modulo-6 counter，it count the clock ticks by using 0,2, 4, 3,5,7，synthesis by D flip-flop in minimal cost.

## Slide 27: Exp.2 a module-6 counter
Q2 | Q1 | Q0 | Q2* | Q1* | Q0*
0 | 0 | 0 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 1 | d | d | d
1 | 1 | 0 | d | d | d
D2=Q1’ ·Q0+Q2’ ·Q1
D1=Q1’
D0=Q2’ ·Q0+Q2·Q1’
Verify the unused state:
Q2Q1Q0=001, Q2*Q1*Q0*=111
Q2Q1Q0=110, Q2*Q1*Q0*=000
These two next states can turn back into the counter’s cycle
counter
Unused
state

## Slide 28: 3、MSI counters and applications
synchronous 4-bit binary counter 74×163
clear
loading
ENT=ENP=CLR_L=LD_L=1，counting
RCO（ripple carry output）:when QDQCQBQA=1111 ，and ENT=1，RCO=1。
hold

## Slide 29: working in free-running mode (modulo-16 counter)
MSB
LSB
74×163 is fully synchronous, its outputs change only on the rising edge of clock.
Counting from 0 to 15

## Slide 30: using 74×163 in m<16 mode counter
Exp：modulo-11 counter
method 1：feedback-clear mode(反馈清零) — count the first m binary numbers from 0000.
key：when counting to the number (m-1), the counter return to 0000 .
so, need a feedback circuit F，and when QDQCQBQA=1010, make CLR_L asserted.
Q0
Q1
Q2
Q3
F=?
CLR_L
74×163
QA
QB
QC
QD
CLR

## Slide 31
Q3 | Q2 | Q1 | Q0 | CLR_L
0 | 0 | 0 | 0 | 1
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1
0 | 0 | 1 | 1 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1
1 | 0 | 0 | 0 | 1
1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0
CLR_L=(Q3·Q2’ ·Q1·Q0’)’
Q0
Q1
Q2
Q3
F
CLR_L
74×163
QA
QB
QC
QD
CLR
CLR_L=(Q3·Q1·)’
For 1011~1111, the CLR_L is deal with don’t care .

## Slide 32: verify the unused state
Unused states 1011~1111:
1011
0000
1100
1101
1110
1111
0001
0010
0110
1010
1000
…
…
…
It can run automatically.
CLR_L=(Q3·Q1)’

## Slide 33: using 74×163 in m<16 mode counter
Method 2：feedback-load mode(反馈置数)—count the last m states or arbitrary m continual states between 0000 and 1111.
key：make LD_L asserted when counting to the ending state, and the initial state is loaded.
①if the ending state is 1111，use the RCO output to reload the initial state.
Initial state=ending state – counting modulo + 1
=15-11+1=5
So all the counting state is 0101~1111.

## Slide 34: reference circuit of feedback-load

## Slide 35
②if the ending state isn’t 1111, then we need to set an initial state and an ending state.
  initial state = ending state – modulo + 1
  or, ending state = initial state + modulo - 1
like，knowing the ending state is 13，so the initial state = 13-11+1=3
or, knowing the initial state is 2，so the ending state =2+11-1=12
circuit design：be similar to feedback-clear mode, but its output need to be connected to the LD_L of 74×163.

## Slide 36: reference circuit of feedback-load
counting from 3 to 13(0011~1101)

## Slide 37: 74×163 cascading application
if the counting modulo >16，multiple 74×163 could be cascaded.
  key：counting nesting(嵌套)
  n pieces of 74×163 →maximum modulo 16n。
connecting lower grade counter’s RCO output to next higher grade counter’s EN signal.

## Slide 38: Modulo-256 free-run counter

## Slide 39: 16<modulo<256 counters
Exp，a modulo-125 counter
methods：
feedback-clear — 0~124；
feedback-reload — 131~255，or arbitrary two numbers whose difference is 124 between 0 and 255.

## Slide 40: Circuit for “feedback-clear — 0~124”
U1
74HC163N_6V
QA
14
QB
13
QC
12
QD
11
RCO
15
A
3
B
4
C
5
D
6
ENP
7
ENT
10
LOAD
9
CLR
1
CLK
2
U2
74HC163N_6V
RCO
15
ENP
7
ENT
10
LOAD
9
CLR
1
CLK
2
U3
74HC30
D7
D6
D5
D4
D3
D2
D1
D0
clock
R1
1k
5V
R2
1k
5V
A
3
B
4
C
5
D
6
QA
14
QB
13
QC
12
QD
11
rco1

## Slide 41: Waveform for modulo-125 counter

## Slide 42: From counter to timer
555多谐振荡器
或
与非门构成的双稳电路
74×162
n
Modulo-6
clock
T=1s
Modulo-60
BCD-7 segment decoder
displayer
74LS48
或
74LS49
共阴型LED
Modulo-10
carry

## Slide 43: An n×m modulus counter
2018/6/6
43
clock
…
…
QL
QH
Q0
Qi
RCO
EN
Modulo n
Q0
Qj
RCO
EN
Modulo m
RCO
Please implement the 6×10 modulus counter with 74x162
74xx162: synchronous BCD decade counter synchronous reset and loading
74xx162
QA
14
QB
13
QC
12
QD
11
RCO
15
A
3
B
4
C
5
D
6
ENP
7
ENT
10
LOAD
9
CLR
1
CLK
2

## Slide 44: Other counters
74×161，asynchronous clear 4-bit binary counter.
asynchronous clear ：if CLR_L=0，QDQCQBQA output 0000 immediately .
other function is as the same as 74×163. use 74×161 to modulo-11 in feedback-clear mode，count ending = 1011，
Counting N | Q3Q2Q1Q0
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 1010
11 | 1011

## Slide 45: Other counters
decades counter
74×160（asynchronous clear）
74×162 (fully synchronous)
74×169 4-bt up/down counter
74x160/162

## Slide 46: 4、decoding binary-counter states
Combine a binary counter with a decoder to obtain a set of 1-out-of-m-coded signals.
Sequential pulse generator

## Slide 47: supplement：sequence generator
design a sequence-generator with 74×163 and 74×151
Exp：a “01100101” sequence-generator
A sequence generator composed of counter & MUX : if the counter is enable, at the each clock tick, circuit output every bit of the sequence.

## Slide 48: design sequence-generator with D F-Fs
设计方法：顺序计数+组合电路
Exp: design a code generator which can output 011010 sequentially。
用顺序计数器的每个计数值产生一个码位。
000 0
001 1
010 1
011 0
100 1
101 0
Q2Q1Q0 | Q2*Q1*Q0* | SEQ
000 | 001 | 0
001 | 010 | 1
010 | 011 | 1
011 | 100 | 0
100 | 101 | 1
101 | 000 | 0
110 | ddd | d
111 | ddd | d
D2 D1 D0
110
111
100

## Slide 49: circuit for sequence-generator in counter mode
U1A
74LS74D
1D
2
1Q
5
1Q
6
1CLR
1
1CLK
3
1PR
4
U1B
74LS74D
1D
2
1Q
5
1Q
6
1CLR
1
1CLK
3
1PR
4
U2A
74LS74D
1D
2
1Q
5
1Q
6
1CLR
1
1CLK
3
1PR
4
U3A
74LS00D
U3B
74LS00D
U3C
74LS00D
U4A
74LS10D
U3D
74LS00D
U5A
74LS00D
U6A
74LS32D
D2
D1
D0
Q2
Q2'
Q1
Q1'
Q0
Q0'
SEQ
clock

## Slide 50: 8.5 Shift Register
An n-bit register with a provision for shifting its stored data by one bit position at each tick of the clock.
Classified by structure：
serial-in, serial-out
serial-in, parallel-out
parallel-in, serial-out
parallel-in, parallel-out
Shift-right
Classified by shifting direction：
Shift-left

## Slide 51: Shift direction
An n-bit number Dn-1Dn-2……D1D0 is stored in an n-bit shift register.
Shift left：shift from LSB to MSB
Shift right：shift from MSB to LSB
Dnew | Dn-1 | Dn-2 | … | … | D1
D0
D1
…
…
Dn-2
Dn-1
Qn-1
Qn-2
Q1
Q0
…
D0
D1
…
…
Dn-2
Dnew
Qn-1
Qn-2
Q1
Q0
shift left
shift right

## Slide 52: 1、shift-register structure
（1）、serial-in, serial-out
After n clock ticks, an input bit appears at the serial output.
it can be used as a pulse-postponed circuit.
input
output
n clock tick
t0
tn

## Slide 53
（2）、serial-in, parallel-out
并出
serial in
parallel out
serial-parallel conversion

## Slide 54
（3）、parallel-in, serial-out
serial out
数据并入
U1
U2
D2
Q1
load/shift=1，load data，Di=iD
load/shift=0，data shift，Di=Qi-1
1
Dn
D1
0
0
1

## Slide 55
（4）、parallel-in, parallel-out

## Slide 56: Detect the signal’s edge with shift register
clock
Din
Detect the posedge
Dout
Detect the negedge
有时，为了避免边沿形状不好导致检测失误，会用2-3级移位寄存器。
D
clock
Q
Din
Dout

## Slide 57: Switch debouncing with shift register
IN
clock
OUT
?
这里输出0或者1，要视具体采集数据的瞬间而定，此处是假设为0

## Slide 58: 2、MSI shift register
74×164, serial-in, parallel-out with asynchronous clear input（CLR_L）.
shift direction
SERA·SERB
RXD
TXD
MCU
U1
74HC164
QA
3
QB
4
QC
5
QD
6
A
1
B
2
CLR
9
CLK
8
QE
10
QF
11
QG
12
QH
13

## Slide 59: MSI shift register
74×194，4-bit bidirectional, parallel-in, parallel-out
Function input | Next state |  |  |  | function
S1S0 | QA* | QB* | QC* | QD* | 
00 | QA | QB | QC | QD | Hold
01 | RIN | QA | QB | QC | Shift right
10 | QB | QC | QD | LIN | Shift left
11 | A | B | C | D | load
注意：此处的左移（QD到QA）、右移（QA到QD）是针对该器件定义的，与数据单元的左/右移不同。
Q3
Q1
Q2
Q0
应用中，习惯性按照数据移位方向命名，即右移是从高到低，因而QA——Q3

## Slide 60: 3、application of shift register: serial/parallel conversion
control circuit
parallel-serial conversion
parallel-in data
parallel-serial conversion
control circuit
parallel-out data
source
destination
serial data
clock signal
synchronous signal

## Slide 61
数字式程控交换机的时分多路复用系统。

## Slide 63: 5、shift-register counters
be differ from the binary up or down counters.
ring counter
an n-bit shift register can be used to obtain a counter with n states.
4-bit ring counter
Q0*=D0=Q3 Q1*=D1=Q0 Q2*=D2=Q1 Q3*=D3=Q2
D
Q
Q
CLK
clock
Q0
Q1
Q2
Q3
D
Q
Q
CLK
D
Q
Q
CLK
D
Q
Q
CLK

## Slide 64: ring counter
initial state：Q3Q2Q1Q0=0001
Q3Q2Q1Q0 | Q3*Q2*Q1*Q0*
0001 | 0010
0010 | 0100
0100 | 1000
1000 | 0001
（D1）Q0
（D2）Q1
（D3）Q2
（D0）Q3
clock
Q0
Q1
Q2
Q3
D
Q
Q
CLK
D
Q
Q
CLK
D
Q
Q
CLK
D
Q
Q
CLK
D0
D1
D2
D3

## Slide 65: State diagram of ring counter
A single circle including 4 states could be used as a modulo-4 counter. (by using 4 F-Fs)
(是顺序脉冲发生器的一种)
0001
0010
0100
1000
normal cycle
Not self-correcting
0011
0110
1100
1001
0111
1110
1101
1011
0101
1010
0000
1111
Abnormal cycle

## Slide 66
use MSI shift register to implement a ring counter
RESET=1，load ABCD=0001；
RESET=0，shift left
State:
Q3Q2Q1Q0
0001
0010
0100
1000

## Slide 67: Self-correcting ring counter
0 | 0 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 1 | 1
0 | 0 | 1 | 1
D0
Q3Q2
Q1Q0
00
01
11
10
00
01
11
10
Not self-correcting
Modify the counting circle
0011
0110
1100
1001
0111
1110
1101
1011
0101
1010
0000
1111
0001
0010
0100
1000
1 | 0 | 0 | 1
0 | 0 | 0 | 0
0 | 0 | 0 | 0
0 | 0 | 0 | 0
D0
Q3Q2
Q1Q0
00
01
11
10
00
01
11
10
D0=Q2’ ·Q1’ ·Q0’

## Slide 68: Self-correcting ring counter
Change the feedback circuit connected to D0.
将环形计数器的低三位经或非门连到LIN端构成校正电路，即LIN=Q2’ ·Q1’ ·Q0’。
So, it is a self-correcting ring counter.

## Slide 69
If the ring counter adopt active-low 1-out-of-n code, then the self-correcting circuit is a 3-input NAND gate which has Q0~Q3 input.
1110
1101
1011
0111

## Slide 70: 7、Johnson Counters (twisted-ring counter）
stucture
D0
D
CLK
Q
Q
CLR
PR
D
CLK
Q
Q
CLR
PR
D
CLK
Q
Q
CLR
PR
D
CLK
Q
Q
CLR
PR
Q0
Q1
Q2
Q3
CLK
Transition equation：
Q0*=D0=Q3’ Q1*=D1=Q0 Q2*=D2=Q1 Q3*=D3=Q2

## Slide 71: State diagram of normal cycle
Set initial Q3Q2Q1Q0=0000，
An n-bit Johnson counter has 2n state. It could be used as a modulo-8 counter.
Q3Q2Q1Q0
0000
0001
1100
1000
0011
0111
1110
1111

## Slide 72: Timing diagram
Each Qi output a pulse which has 8 times of the clock period and 50% duty cycle.
也可作为顺序脉冲发生器

## Slide 73: Johnson counter by using 74x194
RESET_L=0，clear
RESET_L=1，so S1S0=10 make the shift register shift left，Q3Q2Q1Q0：0000—0001—0011—……—1000。

## Slide 74: Johnson counter state decoder
state | Q3 | Q2 | Q1 | Q0 | decording
S1 | 0 | 0 | 0 | 0 | Q3’·Q0’
S2 | 0 | 0 | 0 | 1 | Q1’·Q0
S3 | 0 | 0 | 1 | 1 | Q2’·Q1
S4 | 0 | 1 | 1 | 1 | Q3’·Q2
S5 | 1 | 1 | 1 | 1 | Q3·Q0
S6 | 1 | 1 | 1 | 0 | Q1·Q0’
S7 | 1 | 1 | 0 | 0 | Q2·Q1’
S8 | 1 | 0 | 0 | 0 | Q3·Q2’
Each state can be decoded with a 2-input AND or NAND gate. The output are glitch free.
Johnson counter
CLK
decoder
Q3
Q2
Q1
Q0
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7

## Slide 75
Q3 | Q2 | Q1 | Q0 | Y7 | Y6 | Y5 | Y4 | Y3 | Y2 | Y1 | Y0 | decording
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | Q3’·Q0’
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | Q1’·Q0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | Q2’·Q1
0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | Q3’·Q2
1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | Q3·Q0
1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | Q1·Q0’
1 | 1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | Q2·Q1’
1 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | Q3·Q2’

## Slide 76: Self-correcting Johnson counter
The other 8 unused state is abnormal cycle.
Neither normal cycle nor abnormal cycle is self-correcting.
0101
1011
1001
0010
0110
1101
0100
1010
Q3Q2Q1Q0

## Slide 77: Self-correcting Johnson counter: feedback to load
When current state Q3Q2Q1Q0 is 0××0, the circuit loads 0001 as the next state.
0000
0001
1100
1000
0011
0111
1110
1111
0101
1011
1001
0010
0110
1101
0100
1010

## Slide 78: Self-correcting Johnson counter

## Slide 79: Self-correcting Johnson counter 2:
2018/6/6
79
Make some abnormal states turn into the normal cycle.
0000
0001
1100
1000
0011
0111
1110
1111
0101
1011
1001
0010
0110
1101
0100
1010
1 | 0 | 0 | 0
1 | 1 | 0 | 1
1 | 1 | 0 | 1
1 | 0 | 0 | 0
D0
Q3Q2
Q1Q0
D0=Q3’ ·Q2’+Q3’ ·Q0+Q2’ ·Q0

## Slide 80: Applying shift register to sequence-detecting and sequence-generating
Exp1. A circuit output 1 when its serial input X gets continuous 1010, try to implement it with shift register。
data shift left
detector
Circuit 1.
1
1
0
0

## Slide 81: Applying shift register to sequence-detecting and sequence-generating
data shift right
detector
The same exp. with another implement circuit.
Circuit 2.
1
1
0
0

## Slide 82: Supplement: Sequence generator
The structure of a sequence generator implementing with shift register.
序列输出F
通常，序列的长度即为电路的状态个数，按状态个数S确定触发器（状态变量）个数n，以连续的n位bit为一个状态，在所需生成的序列中按照依次移动1bit的顺序找出S个独立的状态。
Next bit generator
1
1
out
n-bit Shift register
clk
current state
n

## Slide 83
Exp 2：a circuit output sequence 011010011010 … continuously, try to implement it with D flip-flops.
How to find all states?
……0 1 1 0 1 0 0 1 1 0 1 0……
Q2 | Q1 | Q0 | Q2* | Q1* | Q0* | D0(F)
0 | 1 | 1 | 1 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0 | 1 | 1
1 | 0 | 1 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0 | 0 | 0
1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 1 | 1 | 1
0 | 0 | 0 | d | d | d | d
1 | 1 | 1 | d | d | d | d
D2=Q1
D1=Q0
D0=Q2·Q0’+Q2’·Q1’
The sequence is 6-bit long.
So need 6 states to generate each bit at least.
3-bit state variable → 3-bit shift register

## Slide 84
Judge whether the circuit is self-correcting or not：
Q2Q1Q0=000 → Q2*Q1*Q0*=001
Q2Q1Q0=111 → Q2*Q1*Q0*=110
It do goes into a valid state

## Slide 85
Exp3. please generating a sequence 1001101011 with shift register.
Solution：use each current state to generate the next bit which is going to shift in.
Q3Q2Q1Q0 | Q3*Q2*Q1*Q0* | D0
1001 | 0011 | 1
0011 | 0110 | 0
0110 | 1101 | 1
1101 | 1010 | 0
1010 | 0101 | 1
0101 | 1011 | 1
1011 | 0111 | 1
0111 | 1110 | 0
1110 | 1100 | 0
1100 | 1001 | 1
A 10-bit sequence 1001101011
Set 10 states
Next bit
D0
Q
D1
Q
D2
Q
D3
Q

## Slide 86: Exp 4
Design a FSM circuit, it generates a sequence 100110000011, and implement it with shift register
Solution:
  110110000011
12bit
12 states , need 4bit shift register
right
1101
1011
0110
1100
1000
0000
0000
0001
0011
0111
1111
1110
?
?

## Slide 87: Exp 4
Redefine the states: 110110000011
5-bits per a state, so
  11011→10110→01100→11000→10000→00000
  →00001→00011→00111→01111→11110→11101

## Slide 88: 8、 linear feedback shift-register counters
ab. LFSR，normally be called maximum-length sequence generator. It can have 2n-1 states (exclude all 0s state).
structure：

## Slide 89
Also be called Pseudo-random pattern generator
Exp：n=3，the feed-back equation is X3=X1⊕X0
D1
Q
D2
Q
D3
Q
CLOCK
OUT
X3
X2
X1
X0
CLK
OUT
X2 | X1 | X0
1 | 0 | 0
0 | 1 | 0
1 | 0 | 1
1 | 1 | 0
1 | 1 | 1
0 | 1 | 1
0 | 0 | 1
Need a initial state (not all 0s)

## Slide 90: 8.6 iterative versus sequential circuits
the iterative circuit
CI
CO
PI
PO
C0
C1
PI0
PO0
CI
CO
PI
PO
PI1
PO1
CI
CO
PI
PO
PIn-1
POn-1
Cn
C2
…
Cn-1
boundary input
cascading input
cascading output

## Slide 91
using flip-flops to store the cascading outputs at the end of each step
Ci
CI
CO
PI
PO
PIi
POi
register
Ci+1
CLK

## Slide 92: Serial comparator circuit
D1
Q
CLOCK
CMP
X
EQI
Y
EQO

## Slide 93: Serial adder
1-bit
Full
adder
D
CLK
Q
X
Y
Ci
S
Co
Xi
Yi
Ci
Si
Ci+1
clock

## Slide 94: Serial parity circuit
D
CLK
Q
Xi
clock
ODD

## Slide 95: 8.7 synchronous design methodology
Complex digital system
partition
Data unit
Control unit
Synchronous system structure
store
Route(通路)
combine
process
……
start/stop
testing conditions
Deciding what to do next according to circumstance
……
Be designed as state machine
Be handle at a higher level of abstraction

## Slide 96: 8.8 impediments to synchronous design
Clock skew
  Clock signal arrived at each flip-flop has different propagation
  May cause metastable and produce an unpredictable output
Gating the clock
  Suppress(压制) the clock input when it’s not supposed to be loaded

## Slide 97: Summary for chapter 8
Counters
  Modulo-m counters
  Ripple counters
    Up/down counter’s Structure, timing diagram
  Synchronous counters
    Structure, timing diagram
  MSI counters
    74x163, 74x161, 74x169……,
    Function, enable input and RCO output
    Free-running counter
    Modulo-m counter, m<16n(n=1, 2…)

## Slide 98
Shift registers
  Structure, function
  Shift register counters
    Ring counter
    Johnson counter
  Sequence detector
Applications of counters and shift registers
  Sequence generator
    Implement with counter and combinational circuit
    Implement with shift registers

## Slide 99: Class exercise
Design a modula-24 counter with 74*163 and some gates, please realize it by two types of circuit at least. (assume it starts at 00000)
Design a sequence generator which output 10001010, please synthesis this circuit with shift register.

## Slide 100: 课堂练习
2018/6/6
100
（1）设计一个序列信号检测器，当电路的输入端X收到连续的“1011”时，输出F为1，并且状态可以重叠。状态赋值采用QmQm-1…，按gray码序。
（2）设计一个5进制加/减计数器，当控制信号C=0，计数器按加1计数，当C=1，计数器按减1计数。用D触发器综合。