## Slide 1: Chapter 9 Memory、CPLD and FPGA
本章要求:
存储器中的ROM及其用于组合逻辑电路的设计；
ROM, RAM的地址和存储容量的关系，以及容量的扩展等基本知识。

## Slide 2: memory
ROM
(read-only memory)
RAM
(random-access memory)
Non-volatile while powered down
Volatile while powered down
Often be used store firmware or initial program of the computer…
Data exchange and storing temporarily in CPU or other microprocessor
memory：store bits in a structured way

## Slide 3: 9.1 Read-Only Memory (ROM)
1. basic structure
n-bit address (input)
b-bit data (output)
A0
A1
A2
An-2
An-1
D0
D1
Db-1
…
…
0100….1011
D0
Db-1
…
0…00
n-bit address
0…01
1…11
×××××
×××××
b-bit data
sketch map of RAM
2n words × b bit ROM
2n
words
the data input and output in parallel.

## Slide 4: 2. Internal ROM structure
storage array （2n×b）
…
0
1
2n-1
address input
Row (address) decoder
…
A0
A1
An-1
…
D0
Db-1
output circuit
…
Data output

## Slide 5
word line
bit line
address decoder
输出电路
address input
a data stored unit
Data output
has diode: store 1
no diode: store 0
8×4 ROM structure
data stored array

## Slide 6: MOS transistors as storage elements
A transistor means a ‘1’
Nothing means a ‘0’
When address bits are increased, the chip’s physical dimensions are closed to a narrow rectangle.

## Slide 7: 3. Two-dimensional decoding
128 words×1 bit ROM
0000000~0001111
0010000~0011111
1110000~1111111
……
地址位数较多, 采用二维译码方式

## Slide 8: Example: a 32Kx8 ROM
215 word×1 bit
two-dimensional address decode

## Slide 9: 4. commercial ROM types
mask-programmable ROM
  array connections are programmed during semiconductor manufacture using a mask. very fast. very dense. expensive, 2-4 week turn-around, low power
Programmable ROM(PROM)
  fuses to program once in the field, use PROM programmer, inexpensive
word line
bit line
fuse

## Slide 10
EPROM（Erasable PROM）
  fuses implemented using floating-gate MOS transistors to program 10k~100k times in the field, erased by flooding with UV light.

## Slide 11
E2PROM（Electrically EPROM）
  byte-program, individual stored bits may be erased electrically.
    2764(8k×8), 27128(16k×8), 27256(32k×8), 27512(64k×8)
flash EPROM
  a specific type of EPROM which can be erased in large blocks
  NOR type and NAND type
    NOR flash allows a single machine word (byte) to be written or read independently
    NAND flash is programmed and read in pages, and erased in blocks.
solid-state drives (SSDs)
USB device

## Slide 12: Exp. NAND flash ROM’s structure
Bit-storage unit
A block of an NAND flash ROM

## Slide 13: Array organization of a 2GB NAND flash ROM
（Main Area）
（Spare Area）

## Slide 14: Others about EEPROM
按照数据的输入/输出分为串行EEPROM和并行EEPROM。
  串行EEPROM：在读写数据时，输入/输出时通过2线、3线、4线或SPI总线等接口方式进行的。
  并行EEPROM：数据的输入/输出是通过并行总线进行的。
近期，低功耗，写入/擦除速度快的产品很多，如Microchip公司的新型8千位、16千位串行EEPROM，最快时钟10MHZ，写入时间5ms，电流3mA,内置写保护功能，可保存数据达200年，承受100万次擦写。Atmel公司的AT24C××系列……

## Slide 15: 5. Using ROM for “random” combinational logic functions
Store the output value of a given truth table in the ROM, the function inputs are connected to the address input .
Exp1: the dual polarity decoder.(P.801)
POL | I1 | I0 | Y3 | Y2 | Y1 | Y0
0 | 0 | 0 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0 | 0 | 1
8×4 ROM
A0
A1
A2
D0
D1
D3
D2
POL
I1
I0
Y0
Y1
Y2
Y3

## Slide 16: Exp2: 4×4 multiplier
每行第一个数据单元的地址
每行包含16个数据单元的数据

## Slide 17: More Exp.: ROM在同步时序电路设计中的应用
位序列信号的产生：计数器 — ROM法
设计一个码长为8位的序列信号发生器，信号序列为01111110。
CLK
CLR
LD
ENP
ENT
D
C
B
A
QC
QD
QB
QA
RCO
ADD2
ADD1
ADD0
SEQ
VCC
CLK
…
D0
D1
D2
D3
8×4ROM
74××163

## Slide 18: Function table for the sequence generator with ROM
address QC QB QA | Data stored in ROM D3~D0
000 | 0000
001 | 0001
010 | 0001
011 | 0001
100 | 0001
101 | 0001
110 | 0001
111 | 0000
For n-bit ROM, it can implement n outputs logic function.

## Slide 19: ROM在组合电路设计中的应用举例
Try to use 8×4ROM to realize the following function:
F1=AB+A’C, F2=AB+B’C
Solution:
  transform the equation to canonical form first
  put the input variable on the address line of ROM,
  Store the F1, F2
用16字×4位ROM实现2输入变量的与非、或非、异或和同或
实现4位二进制码—格雷码的转换

## Slide 20: Random-access memory (RAM)
Static RAM
Dynamic RAM
both are volatile
Random access means:
locations in the memory can be written to or read from in any order, regardless of the memory location that was last accessed.
store a bit of data in the state of a flip-flop
store a bit of data as a charge in a capacitor

## Slide 21: 9.3 Static Random-Access Memory
2n word ×b bit RAM structure
A0
A1
Din0
An-2
An-1
D0
D1
Db-1
…
Dinb-1
…
CS
OE
WE
Address inputs
Data inputs
Control inputs
Data outputs
×××××
D0
Db-1
…
0…00
An-1…A0
0…01
1…11
×××××
×××××
CS、OE有效，b位数据输出
CS、WE有效，b位数据输入
…
…

## Slide 22: SRAM internal structure
Address decoder
…
A0
A1
An-1
…
Storage array (M×b)
…
D0
Db-1
Output circuit
…
0
1
M-1
D0
Db-1
…
WR/RD
control
WE_L
CS_L
OE_L

## Slide 23: A static-RAM cell
SEL_L、WR_L both negated, D latch hold the data；
SEL_L is asserted, WR_L is negated,tri-state buffer enable, data output (read);
SEL_L、WR_L both be asserted, D latch open, a new bit is stored (write).

## Slide 24: synchronous SRAM
A bit of storage is also a latch.
Put registers in front of address and control (and maybe data) interface, and operation is performed during a clock period.

## Slide 25: 9.4 dynamic RAM
Write:
Charge the capacitor--- store 1;
Discharge the capacitor---store 0.
Read:
  - Precharge bit line to VDD/2.
  - Take the word line HIGH.
  - Detect whether current flows into or out of the cell.
  - Note: cell contents are destroyed by the read!
  - Must write the bit value back after reading.
store a bit of data in a separate capacitor through a MOS transistor, and need to be refreshed periodically.

## Slide 26: SDRAM
Control and data operations are referenced to a common clock signal.
  是single data rate, 与系统总线速度同步，在一个时钟周期的上升沿传输一次数据。
  曾经是PC电脑上最为广泛应用的一种内存类型 ，分为PC66、PC100、PC133等不同规格，而规格后面的数字就代表着该内存最大所能正常工作系统总线速度

## Slide 27
双数据传输模式同步动态随机存储器，即DDR SDRAM (Double Data Rate Synchronous Dynamic Random Access Memory)
  是一种继SDRAM后产生的内存技术，为具有双倍数据传输率之SDRAM，其数据传输速度为系统频率之两倍，由于速度增加，其传输效能优于传统的SDRAM。
  一个时钟周期内传输两次次数据，它能够在时钟的上升期和下降期各传输一次数据 。

## Slide 28: Memory expanding
1. bit expanding
例：从1024×4bit扩展为1024×8bit
解：将4比特的芯片增加一片，地址线接至两片芯片的相同的地址端。
2114芯片位扩展
D0
D1
D2
D3
D4
D5
D6
D7
CS
R/W
A
A
0
9
L
0
A
W
/
R
CS
9
A
2114（I）
数据输出
CS
R/W
A
A
0
9
L
2114（Ⅱ）
D0
D1
D2
D3
D0
D1
D2
D3

## Slide 29
2.word expanding
例：从1024×4bit扩展为4096×4bit
2114芯片字扩展
2-4
译
码
器
D0
A10
A11
R/W
A9… A0
A11 A10=10
A11 A10=11
A11 A10=01
A11 A10=00
D3… D0
CS
R/W
A
A
0
9
L
2114（1）
D0
D1
D2
D3
CS
R/W
A
A
0
9
L
2114（2）
D0
D1
D2
D3
CS
R/W
A
A
0
9
L
2114（3）
D1
D2
D3
CS
R/W
A
A
0
9
L
2114（4）
D0
D1
D2
D3

## Slide 30: 3. word-bit expanding
Exp. Use HM6264 SRAM(8k×8) to construct a 32k×16 memory.
Solution:
  Need two chips to construct a 8k×16 memory block
  And need 4 groups 8k×16 block
  assign the address A14~A0 and data output D15~D0

## Slide 31
2-4
译
码
器
A13
A14
A12…A0
WE
OE
CS1
CS2
…
IO7…IO0
A12…A0
WE
OE
CS1
CS2
…
IO7…IO0
A12…A0
WE
OE
CS1
CS2
…
IO7…IO0
…
6264(1)
6264(3)
6264(7)
A12..A0
D7
D0
…
D7
D0
…
D7
D0
…
CS
A12A0=11
A12A0=10
A12A0=01
A12A0=00
A12…A0
WE
OE
CS1
CS2
…
IO7…IO0
A12…A0
WE
OE
CS1
CS2
…
IO7…IO0
A12…A0
WE
OE
CS1
CS2
…
IO7…IO0
…
6264(1)
6264(3)
6264(7)
D15
D8
…
D15
D8
…
D15
D8
…
WE
OE